## Slide 1: Proposal to clarify Power Class control logic
T-Mobile USA, Apple, Verizon, Skyworks Solutions, Inc., Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #105 R4-2220002
Toulouse, France, 14 – 18 November 2022

## Slide 2: Background
When PC1.5 was introduced in 38.101-1 v16.5.0 [1], 0.5*maxUplinkDutyCycle-PC2-FR1 was used as the duty cycle threshold for PC1.5 to fall back to PC2
The applicability of maxUplinkDutyCycle-PC2-FR1 to PC1.5 was not explicitly documented in 38.306, although it was implicitly because the definition points to clause 6.2.1 of TS 38.101-1.
maxUplinkDutyCycle-PC1dot5-MPE-FR1 was added for PC1.5 FWA (for which MPE rather than SAR applies when > 20 cm from the human body) in 38.101-1 v17.3.0 [3].
There are devices in the field that use 0.5*maxUplinkDutyCycle-PC2-FR1 for PC1.5

## Slide 3: Original Power class logic from 6.2.1 of 38.101-1 v17.2.0
If a UE supports a different power class than the default UE power class for the band and the supported power class enables the higher maximum output power than that of the default power class:
- if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 50% (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle-PC2-FR1 as defined in TS 38.331 (The exact evaluation period is no less than one radio frame); or
- if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the default power class or lower;
- shall apply all requirements for the default power class to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
- else if the UE does not support a power class with higher maximum output power than PC2; or
- if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 25% (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 0.5*maxUplinkDutyCycle-PC2-FR1 (The exact evaluation period is no less than one radio f rame); or
if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the power class 2 or lower;
- shall apply all requirements for power class 2 to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
- else shall apply all requirements for the supported power class and set the configured transmitted power as specified in clause 6.2.4.

## Slide 4
PC≠PC3?
Duty cycle >maxUplinkDutyCycle-PC2-FR1?
Y
Y
N
N
Y
PMax present?
N
Y
PMax≤23?
N
maxUplinkDutyCycle-PC2-FR1 absent?
N
PC2 applies
UL Duty cycle >50%?
Y
N
Y
PC3 applies
PC>PC2?
Duty cycle >0.5*maxUplinkDutyCycle-PC2-FR1?
Y
N
Y
PMax present?
N
Y
PMax ≤ 26?
maxUplinkDutyCycle-PC2-FR1 absent?
UL Duty cycle >25%?
Y
N
Y
N
Y
N
PC1.5 applies
N
Power Class Logic with PC1.5 for based on 38.101-1 v17.2.0
Start
From R4-2000426, text modified for clarity
UL duty cycle is the actual scheduled uplink duty cycle
maxUplinkDutyCycle-PC2-FR1 is the UE capability IE

## Slide 5: Power class logic from 6.2.1 of 38.101-1 after maxUplinkDutyCycle-PC1dot5-MPE-FR1 was added
If a UE supports a different power class than the default UE power class for the band and the supported power class enables the higher maximum output power than that of the default power class:
- if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is absent and the field of UE capability maxUplinkDutyCycle-PC1dot5-MPE-FR1 is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 50% (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle-PC2-FR1 as defined in TS 38.306 (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle-PC1dot5-MPE-FR1 is not absent and half the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle-PC1dot5-MPE-FR1 as defined in TS 38.306 (The exact evaluation period is no less than one radio frame); or
- if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the default power class or lower;
- shall apply all requirements for the default power class to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
- else if the UE does not support a power class with higher maximum output power than PC2; or
- if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is absent and the field of UE capability maxUplinkDutyCycle-PC1dot5-MPE-FR1 is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 25% (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle-PC2-FR1 is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 0.5*maxUplinkDutyCycle-PC2-FR1 (The exact evaluation period is no less than one radio frame); or
- if the field of UE capability maxUplinkDutyCycle-PC1dot5-MPE-FR1 is not absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle-PC1dot5-MPE-FR1 as defined in TS 38.306 (The exact evaluation period is no less than one radio frame); or
- if the IE P-Max as defined in TS 38.331 [7] is provided and set to the maximum output power of the power class 2 or lower;
- shall apply all requirements for power class 2 to the supported power class and set the configured transmitted power as specified in clause 6.2.4;
- else shall apply all requirements for the supported power class and set the configured transmitted power as specified in clause 6.2.4.

## Slide 6
PC > PC3?
UL Duty cycle >maxUplinkDutyCycle-PC2-FR1?
Y
Y
N
Y
PMax present?
N
PMax≤23?
N
maxUplinkDutyCycle-PC2-FR1 absent?
N
Y
PC3 applies
N
Start
maxUplinkDutyCycle-PC1dot5-MPE-FR1 absent?
0.5*UL duty cycle>maxUplinkDutyCycle-PC1dot5-MPE-FR1?
Y
N
Y
N
N
UL Duty cycle >50%?
Y
Y
PC>PC2?
UL Duty cycle >0.5*maxUplinkDutyCycle-PC2-FR1?
Y
Y
N
Y
PMax present?
N
PMax≤26?
N
maxUplinkDutyCycle-PC2-FR1 absent?
N
Y
PC2 applies
N
maxUplinkDutyCycle-PC1dot5-MPE-FR1 absent?
UL Duty cycle>maxUplinkDutyCycle-PC1dot5-MPE-FR1?
Y
N
Y
N
N
UL Duty cycle > 25%?
Y
Y
PC1.5 applies
maxUplinkDutyCycle-PC1dot5-MPE-FR1 absent?
Y
N
maxUplinkDutyCycle-PC1dot5-MPE-FR1 absent?
N
Y
Power Class Logic with PC1.5 for based on 38.101-1 v17.7.0
UL duty cycle is the actual scheduled uplink duty cycle
maxUplinkDutyCycle-PC2-FR1 and maxUplinkDutyCycle-PC1dot5-MPE-FR1 are UE capability IEs

## Slide 7: Descriptions in 38.306 and values from 38.331
maxUplinkDutyCycle-PC2-FR1 Indicates the maximum percentage of symbols during a certain evaluation period that can be scheduled for uplink transmission so as to ensure compliance with applicable electromagnetic energy absorption requirements provided by regulatory bodies. This field is only applicable for FR1 power class 2 UE as specified in clause 6.2.1 of TS 38.101-1 [2]. If the field is absent, 50% shall be applied. Value n60 corresponds to 60%, value n70 corresponds to 70% and so on. This capability is not applicable to IAB-MT. | Band | No | N/A | FR1 only
maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 Indicates the maximum percentage of symbols during a certain evaluation period that can be scheduled for uplink transmission so as to ensure compliance with applicable electromagnetic energy absorption requirements provided by regulatory bodies. This field is only applicable for FR1 power class 1.5 UE as specified in clause 6.2.1 of TS 38.101-1 [2]. If the field is absent, UE shall mitigate MPE autonomously by P-MPR or by other means and no restriction on scheduled uplink duty cycle is needed. | Band | No | N/A | FR1 only
maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 ENUMERATED {n10, n15, n20, n25, n30, n40, n50, n60, n70, n80, n90, n100}
maxUplinkDutyCycle-PC2-FR1 ENUMERATED {n60, n70, n80, n90, n100} OPTIONAL
Based on an LS from RAN4 to RAN2 in R4-2114929

## Slide 8: Observations
Observation 1: There is nothing in the logic or capability signalling to indicate if a UE is a FWA or handheld device.
Observation 2: modifiedMPRBehavior bit 3 for n41, n77, n78 and n79 indicates higher antenna isolation and lower MPR, but the use is not limited to FWA
Observation 3: As it stands, the logic for maxUplinkDutyCycle-PC2-FR1 and maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 are nearly identical
  For the PC2/PC3 threshold maxUplinkDutyCycle-PC2-FR1 corresponds to 2*maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16
  For the PC1.5/PC2 threshold 0.5*maxUplinkDutyCycle-PC2-FR1 corresponds to maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16
  There the only real differences are the values

## Slide 9: Comparison
Threshold | Parameter | Effective Values (%)
PC2/PC3 | maxUplinkDutyCycle-PC2-FR1 | (50), 60, 70, 80, 90, 100
PC2/PC3 | 2*maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16Note 1 | 20, 30, 40, 50, 60, 80, 100, 120, 140, 160, 180, 200
PC1.5/PC2 | 0.5* maxUplinkDutyCycle-PC2-FR1 | (25), 30, 35, 40, 45, 50
PC1.5/PC2 | maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 | 10, 15, 20, 25, 30, 40, 50, 60, 70, 80, 90, 100
maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 allows for a wider range of values for the thresholds, but less granularity
Note 1: The logic compares 0.5 times the % of uplink symbols, which is the same as comparing the % uplink symbols with 2*maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16.

## Slide 10: Observations on RAN4 vs. RAN2 specs
Observation 4: In the RAN4 logic, the default behavior for a PC1.5 capable UE is PC2 for duty cycle > 25%, and PC3 for duty cycle >50 %. This is in line with the definition of maxUplinkDutyCycle-PC2-FR1 in 38.306 which says, “If the field (maxUplinkDutyCycle-PC2-FR1) is absent, 50% shall be applied.”
Observation 5: Observation 4 conflicts with the definition of maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 in 38.306 which says, “If the field (maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16) is absent, UE shall mitigate MPE autonomously by P-MPR or by other means and no restriction on scheduled uplink duty cycle is needed.”
Observation 6: If both fields are absent, it is unclear in 38.306 which default behavior applies, although the behavior is clear in 38.101-1

## Slide 11: Observations on RAN4 vs. RAN2 specs (cont.)
Observation 7:
  38.306 says, “This field (maxUplinkDutyCycle-PC2-FR1) is only applicable for FR1 power class 2 UE as specified in clause 6.2.1 of TS 38.101-1 [2].”
  38.306 says, “This field (maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16) is only applicable for FR1 power class 1.5 UE as specified in clause 6.2.1 of TS 38.101-1 [2].
  The logic in 6.2.1 of 38.101-1 shows that both IEs are applied to the logic for both PC2 and PC1.5 UEs.
Observation 8: There is no need to set both fields, but if both are present the logic in 38.101-1 shows that the power class behavior is based on the smaller uplink duty cycle.

## Slide 12: Additional Observations
Observation 9: RAN4 needs to clarify the FR1 power class behavior in 38.101-1 sub-clause 6.2.1, if necessary
Observation 10: After clarifying the FR1 power class behavior in 38.101-1 sub-clause 6.2.1, RAN4 needs to inform RAN2 if any changes to 38.306 are needed to bring the RAN4 and RAN2 specs into alignment and to remove the ambiguity when both fields are absent.
Observation 11: Any changes need to be backwards compatible with legacy UEs and RAN
Observation 12: Clarifying that maxUplinkDutyCycle-PC2-FR1 applies to PC1.5 is backwards compatible with RAN or UE implementations because the relationship has been clear in 38.101-1 since PC1.5 was added in v16.5.0
Observation 13: Removing “UE shall mitigate MPE autonomously by P-MPR or by other means and no restriction on scheduled uplink duty cycle is needed” from the definition of maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 is also backwards compatible, because the power class logic in 38.101-1 does not have any path to such behavior where there is no restriction on scheduled uplink duty cycle.

## Slide 13: Additional Observations
Observation 14: As per the current control logic, a UE needs to do the following if it doesn’t need/want to use the duty cycle scheme:
  1) Signal only maxUplinkDutyCycle-PC2-FR1 as 100%, resulting in 100% duty cycle for PC2 and 50% for PC1.5;
  2) Or signal only maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 as 100%, resulting in 100% for both PC2 and PC1.5;
  3) If both IEs are signalled as 100%, resulting in 100% for PC2 and 50% for PC1.5.

## Slide 14: Discussion
The most straightforward resolution would be to clarify in 38.306 that maxUplinkDutyCycle-PC2-FR1 applies to PC1.5 and to remove the statement from 38.306 about P-MPR applying when maxUplinkDutyCycle-PC1dot5-MPE-FR1 is not present.

## Slide 15: Proposal
Proposal 1: RAN4 to send an LS to RAN2 explaining the situation in detail and asking them to modify 38.306 as follows:
maxUplinkDutyCycle-PC2-FR1 Indicates the maximum percentage of symbols during a certain evaluation period that can be scheduled for uplink transmission so as to ensure compliance with applicable electromagnetic energy absorption requirements provided by regulatory bodies. This field is only applicable indicated based on FR1 power class 2 UE and also applicable for FR1 power class 1.5 UE as specified in clause 6.2.1 of TS 38.101-1 [2]. If the field and maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 are both absent, 50% shall be applied as the upper limit of the UL duty cycle for power class 2. Value n60 corresponds to 60%, value n70 corresponds to 70% and so on. This capability is not applicable to IAB-MT. | Band | No | N/A | FR1 only
maxUplinkDutyCycle-PC1dot5-MPE-FR1-r16 Indicates the maximum percentage of symbols during a certain evaluation period that can be scheduled for uplink transmission so as to ensure compliance with applicable electromagnetic energy absorption requirements provided by regulatory bodies. This field is only applicable for FR1 power class 1.5 UE as specified in clause 6.2.1 of TS 38.101-1 [2]. If the field and maxUplinkDutyCycle-PC2-FR1 are both absent, 25% shall be applied as the upper limit of the UL duty cycle for PC1.5UE shall mitigate MPE autonomously by P-MPR or by other means and no restriction on scheduled uplink duty cycle is needed. | Band | No | N/A | FR1 only

## Slide 16: References
[1] R4-2011783, “CR for 38.101-1: Introduction of Power Class 1.5,” T-Mobile USA
[2] R4-2115103, “CR to 38.101-1: Introduction of PC1.5 in Bands n77 and n78 (maxUplinkDutyCycle-MPE-FR1 added),” Qualcomm Incorporated, Verizon, LG Electronics, Skyworks Solutions, Inc, CMCC, Huawei, HiSilicon, Samsung, AT&T
[3] R4-2119859, “Correction to maxUplinkDutyCycle-MPE-FR1 for PC1.5,” Qualcomm Incorporated
[4] R4-2114929, High-power UE (power class 1.5) operation in NR bands n77 and n78 (HPUE_PC1_5_n77_n78)