## Slide 1: 3GPP TSG-RAN WG4 Meeting # 107 R4-2309212 Incheon, Korea, 22 May - 26 May , 2023
Source: Ericsson
Title: Observations of RAN4 MPR Results
Agenda item: 8.28.2.1
Document for: Information

## Slide 2: Analysis method
Analysis was done only for FR1 given the lack of results for FR2 based on excel data v4
For each MPR reduction (enhancement) scheme, at a given carrier frequency, compute the spectral efficiency and search for the matching spectral efficiency in the baseline
  MCS in the plots is the MCS of the FDSS-SE scheme; the MCS for the transparent scheme is typically one less
Look up the SINRs for 10% BLER and the OBOs for the baseline and the enhancement scheme, and compute gain for the scheme as
For each company, according to whether Inner/Outer PRBs are used, whether boosting is used, and for each MCS, take the best gain from all configurations of the scheme (i.e. #PRBs, which filter is used, and which type of transparent scheme is used).
  This step is important: some settings have poor performance, and some good performance, so taking a mean will reduce performance substantially from the best configuration.
  The implication is that the UE may adapt schemes or parameters, and if this is practical is not considered here

## Slide 3: General observations
Only 5 companies providing OBO and BLER results: E///, HW, Nok, QC, vivo
QC’s results have MPR table based baselines for the boosted case, rather than other companies that set the OBO based on the RF sims.
  This may not affect relative trends much, but may drive some misalignment in absolute gains.
Vivo’s results are a bit hard to understand, e.g. baseline 10% BLER SINR being worse than FDSS. Speculating that there could be misentered data in some cases.
  Not including vivo’s results in the analysis

## Slide 4: FDSS-SE vs. Transparent: Without Boosting, 700 MHz & 4 GHZ
Results basically from E/// only
  No results from other companies, except vivo
At 4 GHz,
  some (1/4 – 1/2 dB) gains from both transparent and FDSS-SE in outer PRBs for MCS 1 & 3
    No gain from FDSS-SE over transparent
  FDSS-SE has losses in outer PRBs; transparent schemes have 0 dB gain.
At 700 MHz, 0.7 and 0.9 dB, respectively for transparent and FDSS-SE in outer PRBs at MCS 3
  But no gains otherwise
  FDSS has losses on inner PRBs

## Slide 5: FDSS-SE vs. Transparent: With Boosting, 4 GHZ
E///, Nok, QC results were available
All show reduced gains at highest MCS (8)
  MCS 3 vs. MCS 1 gains do not vary too much
Ericsson and QC show reduced or no gains for inner PRBs for FDSS-SE vs. transparent
  Nokia have the opposite: about 0.5 dB more gain from inner at MCS1.
    Nokia’s transparent baseline performs worse compared to FDSS-SE on inner PRBs
Nokia’s transparent baseline is significantly worse (0.5 to 1 dB) than E///’s and QC’s, which could explain this
E/// show at most ~0.5 dB gain from FDSS-SE
  ~1dB loss is observed for MCS 8 in inner PRBs
Qualcomm show about 0.5 db Inner, 1.0 dB outer gains
Nokia: about 0.5-1 dB gain

## Slide 6: FDSS-SE vs. Transparent: With Boosting, 700 MHZ
E///, Nok, HW results were available
  HW only have results for inner PRBs
E/// and HW reduced gains at highest MCS (8)
MCS 3 vs. MCS 1 gains do not vary too much
Ericsson show worse performance for inner PRBs, while Nokia show better for inner PRBs
E/// show ~1-1.5 dB gain from FDSS-SE on outer PRBs,
  Inner PRBs have essentially no gain
  Note: no results for MCS8 for 700 MHz baseline
Huawei show about 1.3 and 0.8 dB gain for inner PRBs at MCS1 and MCS8, respectively
  No gain or small loss from transparent schemes
Nokia: about 0.5-1 dB gain
  The larger gain seems to be from a degradation in the transparent scheme for MCS 8 on the inner PRBs

## Slide 7: Summary
The spreadsheet results provide a limited window into behavior, since
  A small number of companies provided results
  A limited number of bandwidth and MCS combinations were simulated
  There are many configurations simulated, and selecting among them is complicated, which leads to taking the ‘best’ configuration although this may exaggerate gains.
  Companies do not provide results for all configurations, boosting/not, inner/outer, etc.
Companies providing simulations generally seem to focus on the boosting case
  Only E//, and we understand vivo, provide results for both boosting & non, but others all provide results for boosting
Companies generally found worse gains of FDSS-SE for MCS8, but not much differences between MCS 1 & 3
E/// and QC show reduced or no gains for inner PRBs for FDSS-SE vs. transparent
  Nokia tends to show worse performance for inner PRBs, especially for transparent schemes
E/// and QC tend to show less benefit of FDSS-SE over the transparent schemes compared to HW & Nok
  This could be in part due to the selection of the transparent scheme: HW & Nok use FDSS, whereas E/// and QC use Clipping, Clipping+Filtering, and/or Peak Cancelation
  HW found no benefit at all from transparent schemes