## Slide 1: R19 NR Sidelink continuation and enhancements in RAN4
OPPO
3GPP TSG-RAN4 Meeting #110 R4-2401798 Athens, GR, 26 Feb – 01 Mar, 2024

## Slide 2: Background
In Rel-18, RAN4 has focused on the limited objectives of SL-unlicensed, SL CA, SL inter-band concurrent operation and the LTE/NR SL co-channel co-existence areas due to limited time. And some of the important SL targets have to be deprioritized and postponed to Rel-19.
  For SL-Unlicensed:
    Only power class 5 has been specified for SL-U
    Only 1Tx is supported for SL-U
    Only 5 NS values of 17 in unlicensed spectrum has been specified
  For SL CA
    Only intra-band contiguous CA is supported
    Only power class 3 is supported
  For inter-band con-current operation
    Only band n78@PC3 + band n46@PC5 is defined

## Slide 3: Consideration of R19 continuation/enhancements
To complete the Rel-18 deprioritized targets and also enhance the whole performance of SL, some of RAN4 centric objectives can be considered in Rel-19.
For SL-Unlicensed:
  Power class 3 can be considered to improve UL coverage, and the NR-U requirements can be used as baseline to facilitate discussion
  SL-MIMO and TXD to improve UL throughput considering 2Tx has already been supported for SL from Rel-16, now it is simply extended to unlicensed spectrum
  Continue the left NS values from R18 to cover other regions and countries
For SL CA:
  Introduce intra-band non-contiguous CA, considering there is clear demands for this even in Rel-18 stage from EU vehicular industry
  Introduce power class 2 for SL CA is also important to improve user experience and SL coverage
For inter-band con-current operation :
  Introduce NR Uu band@PC3 + SL-U band@PC3, e.g. n78@PC3 + n46@PC3

## Slide 4: Proposal
Introduce RAN4 centric NR SL enhancements in R19 with below objectives.
For SL CA enhancement
  Introduce intra-band non-contiguous CA in ITS spectrum with power class 3
  Introduce power class 2 for intra-band contiguous CA
For SL-U enhancement
  Introduce power class 3 for NR SL-U
  Introduce SL-MIMO and TxD feature for NR SL-U with both power class 5 and power class 3
  Continue the left NS values from R18 to cover other regions and countries