## Slide 1
Discussion on introduction Power Class 8 (PC8) for FR2
3GPP TSG-RAN WG#4 #114 R4-2501551
Athens, Greece, 17 – 21 Feb., 2025
Agenda Item: 5.1.1
Document for: Decision
Huawei, HiSilicon, CTC, CEPRI, OPPO, vivo, Xiaomi, CATT, Spreadtrum, Google, Honor, TD Tech, StarPoint, SRTC

## Slide 2
Background
  RAN4#110bis ~ RAN4#112bis:
    From RAN4#110bis April meeting to RAN4#112bis Oct meeting, 4 RAN4 meeting cycles with more than half years extensive discussion and evaluations [3], RAN4 reached agreements on introduction of FR2 PC8 in RAN4#112bis [4].
  RAN4#113:
    CRs [6~8] could not be agreed because some company proposed to reconsider the introduction of FR2 PC8 [10]
    Several candidate compromise solutions are discussed, but no conclusion. Some company prefer to discuss it in RAN
  RAN#106
    RAN concluded that RAN4 can continue the discussion on FR2 PC8
  Urgency: Our original motivation is in order to turn the following situation around in FR2
    The FR2 deployment would be limited at least in some countries, even if FR2 has been introduced at the beginning of 5G. In our view, at least one of the root causes would be the number of UEs supporting FR2 is less that would come from the fact that relatively higher cost and more huge power consumption than FR1. The situation stays even in the late of 5G. Hence, without taking any measures, the situation would stay.
    Thus, we believe that it is worth taking a measure to enable more UEs specifically in low and middle-end UEs to support FR2 as early as possible in the late 5G stage.
    The low and middle-end UEs are complementary to high-end UE with simplified RF architecture for power consumption and cost saving. Diversify terminal types in the markets is beneficial to promote the FR2 industry development.

## Slide 3
Analysis of FR2 Power Class 8 – cost and power consumption
FR2 power class 3 (FR2 PC3): typical RF architecture
Typical requirements: EIRP 22.4dBm,
Spherical coverage (50%) 11.5dBm
RF chains：
Two AIPs + IF (Intermediate frequency)
FR2 UE selects one AIP(Panel) out of two, and for each AIP 8 RF analog chains work simultaneously for reception and transmission
Beam management (BM)：
Multiple Rx beams supported, e.g., 7 Rx beams/AIP
Assuming BS has 16 SSB Tx beams，FR2 PC3 UE needs to do measurements for around 160 pairs of Tx-Rx beams for each beam management at least.
Power consumption of FR2 PC3
  Due to multiple analog RF chains and complex BM, power consumption of FR2 PC3 is 3~4 times of FR1, which further may lead to overheating issue
FR2 power class 8 (FR2 PC8): typical RF architecture
Typical RF requirements：EIRP 16.4dBm,
Spherical coverage (50%) 5.5dBm
RF chain：
One AIP + IF (Intermediate frequency)
PC8 uses 1 AIP(panel) with 2 pairs of X-pol antenna elements
Beam management (BM)：
AIP has the spatial coverage like an omni-directional antenna
Assuming BS has 16 SSB Tx beams，FR2 PC8 UE needs do measurements for less than 20 pairs of Tx-Rx beams for each beam management, which is 1/10 of PC3.
RF2 RF architectures |  | FR power mW | Cost $
PC3 | Two AIPs | 3~4X | 2~3Y
PC8 | One AIP | 2X | Y
-- | FR1*200MHz 4-layer | X | Y
  PC8 vs PC3 cost and power consumption comparison
Cost of FR2 PC3
  Adding one FR2 band supporting PC3, the cost is more than 2 times and the power consumption is 3~4 times than adding one FR1 band
  The total price of IF + 2xAIP would be more than $15

## Slide 4
  Spherical coverage
    In our view, spherical coverage requirements are one of the most essential ones in FR2 in terms of coverage
    Though due to hardware/cost constrains, no room to improve peak EIRP/EIS, maybe some room to have a bit better spherical coverage. But extremely high values will make PC8 infeasible and no meaning to introduce it finally.
    We did evaluations on different spherical coverage values with the agreed simulation assumptions [3]
Discussion – Evaluations for different Spherical coverage
SLS performance evaluation (UPT) for UL/200MHz
SLS performance evaluation (UPT) for DL/200MHz
SLS performance evaluation (UPT) for UL/400MHz

## Slide 5
Observations for different Spherical coverage
  The better performance at the cell edge can be achieved with the improved spherical coverage:
    6.58Mbps, 7.59Mbps, 8.95Mbps and 11.8Mbps for spherical coverage 5.5dBm, 6.5dBm, 7.5dBm and 8.5dBm with 200MHz CBW respectively
    The achievable throughput can meet almost all application services request. Even 6.58Mbps@5.5dBm spherical coverage is enough for most applications
    Larger channel bandwidth, such as 400MHz or 800MHz with CA, can be utilized to further improve the throughput to meet some services that require higher throughput.
    We prefer to keep the 5.5dBm spherical coverage considering the same UE RF architecture assumption as PC7, but as a compromise, we are open to discuss other possible spherical coverage requirements.
Application | UL(Mbps) | DL(Mbps)
VOIP video call | 2~5 | 2~5
Chating | 1~2 | 50
Live video | 5~8 | 10
Short video playback | 1~1.5 | 10
Code scan | 0.5 | 12
Navigation | 2 | 6
Games | 0.2 | 17
  We collect the UL/DL throughput request for different applications
  Proposal 1: As a compromise solution, RAN4 can discuss other improved spherical coverage requirements for FR2 PC8.

## Slide 6
Some operator prefer to introduce access control scheme for FR2 PC8 which is similar to 2Rx XR and RedCap and would like to control the UE supporting FR2 PC8 to access their network
The following access control scheme are introduced for 2Rx XR and RedCap UE in SIB1
Discussion on Access control scheme
  Access control in SIB1 for RedCap
    intraFreqReselectionRedCap
    cellBarredRedCap1Rx and cellBarredRedCap2Rx
  Access control in SIB1 for 2Rx XR
    intraFreqReselection2RxXR
    cellBarred2RxXR
  Proposal 2: As a way forward, introduce similar access control scheme as 2Rx XR and RedCap for FR2 PC8
    intraFreqReselectionFR2PC8
    cellBarredFR2PC8
As way forward, we are OK to introduce a similar access control scheme for FR2 PC8:
    intraFreqReselectionFR2PC8
    cellBarredFR2PC8

## Slide 7
  [1] R4-2414420, WF on introduction of new FR2 power class 8, Huawei, HiSilicon, RAN4#112
  [2] R4-2415628, Discussion on introduction of new FR2 UE power class, Huawei, HiSilicon , RAN4#112bis
  [3] R4-2415629, Updated simulation assumptions for introduction of FR2 Power Class 8, Huawei, HiSilicon, RAN4#112bis
  [4] R4-2417183, WF on FR2 Power Class 8, Huawei, HiSilicon, RAN4#112bis
  [5] RP-243021 Motivation on introduction of power class 8 for FR2, RP#106
  [6] R4-2419407, CR on introduction of RF requirements for FR2 power class 8 [FR2_PC8], Huawei, HiSilicon
  [7] R4-2419408, CR on introduction of RRM requirements for FR2 power class 8 [FR2_PC8], Huawei, HiSilicon
  [8] R4-2419409, CR on release independence for FR2 power class 8 [FR2_PC8], Huawei, HiSilicon
  [9] R4-2419410, LS to RAN2 on introduction of FR2 power class 8, Huawei, HiSilicon
  [10] R4-2418873, Reconsidering the proposed new FR2 power class 8 and its specification, Ericsson, Telecom Italia, US Cellular
Reference