## Slide 1
(e)Redcap enhancement in Rel-20
Sony
3GPP TSG-RAN WG4 Meeting #115
Malta, MT, 19th – 23rd May, 2025
R4-2507133
Agenda item:11

## Slide 2: Background
Redcap was specified in Rel-17 with the aim to reduce the complexity compared to legacy NR devices and target use cases like wearable devices, surveillance camera etc.
In Rel-18, further simplification done enabled the eRedcap devices to support use cases towards low-end IoT applications.
No dedicated enhancements on (e)Redcap were introduced in Rel-19 WIs, although multiple proposals were submitted during various stages of the release.
Enhancements aiming to further reduce the device complexity, offer more flexible spectrum allocation and improve upon power saving are needed to enable (e)Redcap devices to address more use cases and larger market opportunities.

## Slide 3: 3MHz CBW support for (e)Redcap
3MHz channel BW was specified for non-Redcap NR device in Rel-18, while the demand of 3MHz for (e)Redcap has also been raised in Rel-19 for n106 for utility applications [1].
Industry is seeking a low cost and low complexity replacement for existing cellular meters in Band n106 - 3 MHz networks using (e)RedCap enabled electric meters.
For utility applications and generally low-end IoT applications, single Rx and/or also HD-FDD can be a natural fit due to the reduced cost and power consumption. Therefore, it will be a great benefit for (e)Redcap devices if 3MHz CBW can be supported for (e)Redcap in Rel-20.
In addition, 3MHz CBW is under specification for NR NTN in Rel-19. Based on the demand from NTN operators, the 3MHz CBW can be specified for Redcap NTN in Rel-20 as well.

## Slide 4: Single SKU design on eRedcap
The HD–FDD design of eRedcap offers the opportunity for SAW-less implementation to enable a single SKU (stock-keeping unit) design for global operation:
  the SAW-less design with single SKU improves the power efficiency of the RF front end.
  streamlines production, lowers inventory costs and achieves economies of scale through higher production volumes.
  facilitates further network deployments and ecosystem growth and enables the eRedcap device towards low-end IoT applications.
However, the single SKU implementation of eRedcap is not possible currently to meet all RF requirements. Therefore, a study on the limiting factors in RF requirements and specify the corresponding mechanism(s) to enable single SKU designs for HD-FDD eRedcap can be carried out in Rel-20.
Power efficiency improvement
Footprint size reduction

## Slide 5: Relaxed RLM and BFD for (e)RedCap UEs
In Rel-17 the relaxed RLM and BFD was specified for non-Redcap UE which can reduce the power consumption in low mobility use cases and/or in good channel conditions [2].
Such a power consumption reduction mechanism will be more critical for IoT type of use cases, for example, utility applications, due to its stationary deployment and the low data rate use cases.
Therefore, it is proposed that to specify relaxed RLM and BFD for (e)Redcap devices in Rel-20.
MO without RLM/BFD measurement relaxation
MO with RLM/BFD measurement relaxation

## Slide 6: Summary
In this contribution, we proposed the following items as RAN4 Rel-20 enhancements for (e)Redcap device:
  RF:
    Specify the 3MHz CBW for (e)Redcap device, including both TN and NTN.
    Study the limiting factors in UE RF requirements in TS 38.101-1 and specify the corresponding mechanism(s) to enable single SKU designs for HD-FDD eRedcap with baseband bandwidth reduction BW3/PR3.
      The mechanism shall guarantee the public safety band protection, and that the corresponding spurious emission for UE co-existence level shall not be relaxed.
  RRM:
    Specify relaxed RLM and BFD for (e)Redcap devices.

## Slide 7: References
[1] RP-242812 Motivation for new WI on less than 5 Mhz (e)RedCap Support in Rel-19 Anterix
[2] RP-242982 Proposal for RRM objective on relaxed RLM/BFD for Redcap Ericsson, MediaTek inc., vivo