## Slide 1: Way Forward on Framework of Rx Core Requirements for Non-Contiguous 4C-HSDPA
Qualcomm Incorporated, Ericsson, Renesas Mobile Europe Ltd, ST-Ericsson
3GPP TSG-RAN WG4 Meeting #62bis R4-122222
Jeju, Korea, 26 – 30 Mar 2012

## Slide 2: In-Gap vs. Out-of-Gap
In-Gap requirements
  Defined as Rx core requirements with blocker(s) located relative to the left subblock with a positive offset or relative to the right subblock with a negative offset, resulting in blocker(s) located in the middle of two subblocks.
Out-of-Gap requirements
  Defined as Rx core requirements with blocker(s) located relative to the left subblock with a negative offset or relative to the right subblock with a positive offset, resulting in blocker(s) located either on the left of left subblock or on the right of right subblock .
C…C
Jammer
C…C
C…C
C…C
Jammer
C…C
C…C
Jammer
Or

## Slide 3: Summary of proposals
Proposal 1: All the carriers shall be measured. The same requirements shall apply for each carrier.
Proposal 2: Re-use REFSENS and maximum input level as the existing requirements.
Proposal 3: For out-of-gap requirements, keep all the existing requirements: ACS, in-band blocking, narrow-band blocking, out-of-band blocking/spurious response, intermodulation and narrow-band intermodulation.
Proposal 4: For in-gap requirements, introduce in-gap ACS, in-band blocking, narrow-band blocking requirements as shown in Annex, and not to specify other Rx core requirements for in-gap requirements.

## Slide 4: Annex: Framework of in-gap requirements

## Slide 5
Scenario A
5 MHz Gap
C…C
ACS
C…C
C: Carrier
ACS: ACS Blocker (Case 1 and 2)
Note1 : Narrow Band Blocking test shall be introduced for the case when in-gap ACS test is introduced, for the applicable bands.

## Slide 6
Scenario B
10 MHz Gap
C…C
ACS
C…C
ACS
C: Carrier
ACS: ACS Blocker (Case 1 and 2)
Note1 : Narrow Band Blocking test shall be introduced for the case when in-gap ACS test is introduced, for the applicable bands.
Note 2: Blockers in the figure shall be put one at a time.

## Slide 7
Scenario C
15 MHz Gap
ACS
ACS
C…C
C…C
IBB
W
C: Carrier
ACS: ACS Blocker (Case 1 and 2)
IBB W: -56 dBm In Band Blocker
Note1 : Narrow Band Blocking test shall be introduced for the case when in-gap ACS test is introduced, for the applicable bands.
Note 2: Blockers in the figure shall be put one at a time.

## Slide 8
Scenario D
20 MHz Gap
ACS
ACS
C…C
C…C
IBB
W
IBB
W
C: Carrier
ACS: ACS Blocker (Case 1 and 2)
IBB W: -56 dBm In Band Blocker
Note1 : Narrow Band Blocking test shall be introduced for the case when in-gap ACS test is introduced, for the applicable bands.
Note 2: Blockers in the figure shall be put one at a time.

## Slide 9
Scenario E
25 MHz Gap
ACS
ACS
C…C
C…C
IBB
W
IBB
S
IBB
W
C: Carrier
ACS: ACS Blocker (Case 1 and 2)
IBB S: -44 dBm In Band Blocker
IBB W: -56 dBm In Band Blocker
Note1 : Narrow Band Blocking test shall be introduced for the case when in-gap ACS test is introduced, for the applicable bands.
Note 2: Blockers in the figure shall be put one at a time.