## Slide 1: Way Forward to UE performance for Multiflow HSDPA
Qualcomm Incorporated, [Ericsson, ST-Ericsson, Renesas Mobile Europe Ltd.]

## Slide 2: System Simulation Assumptions (1)
Parameters | Comments
Cell Layout | Hexagonal grid, 19 Node B, 3 sectors per Node B with wrap-around
Inter-site distance | 1000 m
Carrier Frequency | 2000 MHz
Path Loss | L=128.1 + 37.6log10(R), R in kilometers
Penetration loss | 10 dB
Log Normal Fading | Standard Deviation : 8dB Inter-Node B Correlation:0.5 Intra-Node B Correlation :1.0
Max BS Antenna Gain | 14 dBi
Antenna pattern | Mandatory: = 70 degrees, Am = 20 dB Optional: (3D ant) Kathrein Antenna Pattern with 7 deg downtilt (3D ant) Based on 36.814, table A.2.1.1.2 (*) = 70 degrees, Am = 25 dB = 10, SLAv = 20 dB The parameter is the electrical antenna downtilt. Antenna height at the base station is set to 32m. Antenna height at the UE is set to 1.5 m.

## Slide 3: System Simulation Assumptions (2)
Parameters | Comments
Number of UEs/cell | Large enough to get accurate statistics with multiple dropping UEs dropped uniformly across the system
CPICH Ec/Ior | -10 dB
Total Overhead power | 20% (not including HS-SCCH)
UE Antenna Gain | 0 dBi
UE noise figure | 9 dB
Thermal noise density | -174 dBm/Hz
Maximum Sector Transmit Power | 43 dBm
Transmit Power | When computing the recieved power from each cell, Assume full power (43dBm) for the primary serving and secondary serving cell Assume overhead ([20, 40, 60 80 100]% of 43dBm) for the rest of 55 cells.
Soft Handover Parameters | R1a (reporting range constant) = 6 dB, R1b (reporting range constant) = 6 dB
Maximum active set size | 3
Candidate Schemes | Multiflow schemes: SF-DC Aggregation
UE distribution | UEs uniformly distributed within the system
Secondary serving cell | The secondary strongest cell in the UE active set, based on path loss and shadowing, is the secondary serving cell. For Intra-NB schemes, secondary serving HS-DSCH cell is further restricted to be at the same Node B as the primary serving cell. For Inter-NB schemes, secondary serving HS-DSCH cell could belong to a different NodeB.

## Slide 4: Definition
Ior1: Received signal power from the strongest cell
Ior2: Received signal power from the second strongest cell
Ior3: Received signal power from the thrid strongest cell
Ioc: Received signal power from the rest 54 cells in addition to thermal

## Slide 5: Way Forward
Interested companies are requested to propose scenarios for UE demodulation performance requirements for Multiflow HSDPA in RAN4#66.
  Proposed scenarios will be based on system simulation results with the summarized simulation assumptions.
  System simulations will be based on statistics collection with multiple UE droppings instead of running actual traffic model for simplicity.
  Ior1/Ioc can be binned with 1 dB resolution.
  For each bin with higher probabilities, Ior1/Ior2 and Ior1/Ior3 can be shown.