## Slide 1: Way Forward on SCell Activation/Deactivation Delay
Qualcomm Incorporated, Renesas, Ericsson, ST-Ericsson, Huawei, HiSilicon
R4-130828
3GPP TSG-RAN WG4 Meeting # 66
St. Julian’s, Malta, 28 Jan - 1 Feb, 2013

## Slide 2: Activation/Deactivation Minimum Requirements for Rel.10
Both typical case(cold-start 2) and worst case(cold-start 1) will be captured in 36.133
  Typical case requirement:
    SCell Activation time is 24ms (the UE shall be able to receive DL signals on the SCell and transmit valid UL signals for the SCell at N+24ms where N is the subframe when the SCell activation command is received)
    Side condition:
      UE sent a valid report within max([5] measurement cycles, [5] DRX cycles) before the SCell activation is received by the UE
      SCell remains detectable according to the cell identification conditions in section 8.3.3.2 during this time
  Worst case
    SCell Activation time is 24+X ms, X is the time required to acquire PSS/SSS with -3dB Es/Iot in ETU70, AWGN, EPA5(known cell ID)
      Receive time difference at the UE between PCell and SCell is up to +-31.3us
      Companies to bring proposals for X at RAN4#66-Bis
BS can assume PCell will not be impacted(no interruptions) after N+9 (N is the subframe when the SCell activation command is received by UE)

## Slide 3: How to capture the requirement
Minimum Requirements will be captured in 36.133
  TBD in which section the requirements will be captured
LS will be sent to RAN1/2 to inform them of the RAN4 agreements
  Ask RAN1/2 to update the specifications to reflect the RAN4 agreements
  Indicate in the LS that if a UE performs better than the minimum requirements, this UE and network may benefit from allowing activation of the SCell whenever the UE is ready to do so