## Slide 1: Way forward on BS performance requirements for HSUPA MIMO
Nokia Siemens Networks, Ericsson, ST-Ericsson, Qualcomm Incorporated, Huawei
R4-130838

## Slide 2: General approach
Companies are invited to investigate the option of introducing two separate performance requirements for HSUPA MIMO:
Define BS demodulation performance requirements for HSUPA MIMO Rank-2 transmission
Define performance of TPI generation to subject of the testing feasibility

## Slide 3: BS demodulation performance
  Performance metric
Measured performance characteristic is the throughput (calculated as a fraction of the maximum throughput of the corresponding FRC with the BLER equal to 0%)
The requirements (Rx Ec/No) are defined for the [70]% percentiles of the maximum throughput
The throughput is measured per stream

## Slide 4: BS demodulation performance
  Range of the requirements
Introduce new demodulation performance requirements only for fixed Rank-2 transmissions
Introduce new demodulation performance requirements for E-DPDCH and S-E-DPDCH channels

## Slide 5: BS demodulation performance
  Power control and beamforming
Power of the transmitted signal is constant (the power control mechanism is OFF)
Beamforming (TPI) is fixed during the test duration

## Slide 6: BS demodulation performance
  Fixed reference channels (FRC)
The same FRC is used for both E-DPDCH and S-E-DPDCH channels
Two new FRCs (FRC9, FRC10) derived from existing FRC3 and FRC8

## Slide 7: BS demodulation performance
  FRC9 (boosted E-DPCCH)
Parameter | Unit | Value
Modulation |  | QPSK
Maximum. Inf. Bit Rate | kbps | 8100
TTI | ms | 2
Number of HARQ Processes | Processes | 8
Information Bit Payload (NINF) | Bits | 16200
Binary Channel Bits per TTI (NBIN) (3840 / SF x TTI sum for all channels) | Bits | 23040
Coding Rate (NINF/ NBIN) |  | 0.703
Physical Channel Codes | SF for each physical channel | {2,2,4,4}
E-DPDCH/DPCCH power ratio E-DPCCH/DPCCH power ratio S-DPCCH/DPCCH power ratio S-E-DPCCH/DPCCH power ratio S-E-DPDCH/DPCCH power ratio | dB dB dB dB dB | TBD TBD TBD TBD TBD E-DPDCH/DPCCH power ratio is calculated for a single E-DPDCH with SF 4. The power of an E-DPDCH with SF2 is twice that of an E-DPDCH with SF4.

## Slide 8: BS demodulation performance
  FRC10 (boosted E-DPCCH)
Parameter | Unit | Value
Modulation |  | 16QAM
Maximum. Inf. Bit Rate | kbps | 16218
TTI | ms | 2
Number of HARQ Processes | Processes | 8
Information Bit Payload (NINF) | Bits | 32436
Binary Channel Bits per TTI (NBIN) (3840 / SF x TTI sum for all channels) | Bits | 46080
Coding Rate (NINF/ NBIN) |  | 0.704
Physical Channel Codes | SF for each physical channel | {2,2,4,4}
E-DPDCH/DPCCH power ratio E-DPCCH/DPCCH power ratio S-DPCCH/DPCCH power ratio S-E-DPCCH/DPCCH power ratio S-E-DPDCH/DPCCH power ratio | dB dB dB dB dB | TBD TBD TBD TBD TBD E-DPDCH/DPCCH power ratio is calculated for a single E-DPDCH with SF 4. The power of an E-DPDCH with SF2 is twice that of an E-DPDCH with SF4.

## Slide 9: BS demodulation performance Detailed simulation assumptions
Parameter | Value
Physical channels | DPCCH, S-DPCCH, E-DPCCH, S-E-DPCCH, E-DPDCH and S-E-DPDCH
E-DCH TTI [ms] | 2
Modulation | QPSK, 16-QAM
Channel encoder | 3GPP Release 6 Turbo Encoder
Turbo decoder | Max Log MAP
Number of iterations for turbo decoder | 8
Node B receiver type | Rake and/or LMMSE
Channel estimation | Realistic
Inner loop power control | Off, fixed TX power approach
Outer loop power control | Off
EVM [%] | 0
TX weight vector selection | A fixed precoding weight vector
E-TFC selection | Fixed FRC approach, the same FRC for E-DPDCH and S-E-DPDCH
Propagation channel | Ped A, 3 km/h; Ped B, 3 km/h; Veh A, 3 km/h
Antenna configuration | 2x2
Time Alignment Error at UE | 0Tc
Correlation of channel realizations between TX antennas | 0
Correlation of channel realizations between RX antennas | 0
H-ARQ approach | Incremental redundancy, 4 H-ARQ transmissions at maximum
Metrics | Rx Ec/No at [70]% of max throughput

## Slide 10: TPI generation performance
TPI generation performance can be tested against HSUPA MIMO performance with random TPI
Same simulation assumptions can be used as in BS demodulation performance except TPI generation

## Slide 11: Open issues
Investigate the need for E-DPCCH performance requirements with inter stream interference condition when MIMO configured – in simialar way as existing requirements