## Slide 1: Way forward on Wideband RSRQ
NTT DOCOMO, Ericsson, ST-Ericsson, intel, Anritsu, Renesas
R4-131364
3GPP TSG-RAN WG4 Meeting #66bis
Chicago, USA, 15th – 19th April 2013

## Slide 2: Way forward on condition setup
RE config2 is used for wideband RSRQ testing
  Where, Config2 means that on victim cell,
    CRS of antenna port 0 and 1 are transmitted
    PSS/SSS/PBCH are transmitted
    all other RE are set with zero power
Test parameters for Ês/Iot1 ≥ -3dB
  Y ≥ 5dB, X and Ês/Iot2 is TBD
    Exact value of Y, X, Ês/Iot2 will be decided in the #67 meeting (Fukuoka)
There is no limitation for UE implementation in the number of RBs used for Wider bandwidth RSRQ measurements as long as it is greater than 6 PRBs.
The basis for the Ideal wideband RSRQ value (under conditions where Io is not constant across the channel BW) is FFS
  Measurement accuracy is difference between Ideal wideband RSRQ and measured wideband RSRQ
Frequency
Io1 dBm
Io2 dBm
Io
N = 6 RBs
AllowedmeasBW = 50 RBs
X dB
Wideband RSRQ ≤ (Reference RSRQ - Y dB)

## Slide 3: Company’s view on condition setup
 | configuration | Min RBs assumed | Es/Iot1=-3dB |  |  | 
 |  |  | X | Y | Es/Iot1 | Es/Iot2
Ericsson(R4-131548) | Config 2 | 50 or larger | 8.2 | 5 | -3 | 17
Huawei/HiSiliicon(R4-131120) | Config 1 | 50 | 4.67 | 4.4 | -3 | inf
Intel(R4-131298 ,R4-13069) | Config 2 | 50 | 5.7 | 5 | -3 | 5
Renesas (R4-130109) |  |  |  |  | -3 | 
ZTE (R4-130255) |  |  | 19.76 | 3 | -1.76 | 18
Anritsu (R4-126092) |  |  |  | 4.32 | -3 |