## Slide 1: WF on TS 36.111 Section 6 Requirements
TruePosition, Andrew Corporation
3GPP TSG RAN WG4 #66bis
Chicago, USA, 15th-19th April 2013
Agenda Item: 6.8.1.2
R4-132013

## Slide 2: UL RTOA Requirements with DRX and Dropped SRS
  For further study—possible impacts to measurement time requirements

## Slide 3: UL RTOA Measurement Requirement for TDD
  When Tsrs>2ms, FDD UL RTOA measurement requirements apply also for TDD
  When Tsrs=2ms, the UL RTOA measurement time is as below:

## Slide 4: SRS Configuration Update
  UE SRS configuration may change for one or more cells or a set of cells with the UE SRS may change during UL positioning
  Upon receiving SRS configuration update, the LMU shall continue the UL RTOA measurement for a cell and report the measurement, while meeting the requirements in Section 6, in the following cases:
    the new SRS configuration for the cell is the same as the SRS configuration for this cell before receiving the SRS configuration update
    the new SRS configuration for the cell is a superset of the SRS configuration for this cell received before the update, i.e., the updated SRS configuration comprises the SRS configuration before the update but may also have other SRS configured