## Slide 1: WF on TS 36.111 Section 6 Requirements
TruePosition, Andrew Corporation
3GPP TSG RAN WG4 #67
Fukuoka, Japan, 20-24 April 2013
Agenda Item: 6.8.1.2
R4-132326

## Slide 2: UL RTOA Requirements with DRX
  The current UL RTOA measurement period requirements assume that either the UE is not configured with DRX or that the eNB is coordinating the assigned SRS configuration with the active-time of the UE when in DRX mode.
  Add the following text to Section 6:
    If DRX operation continues during the UTDOA positioning attempt, SRS configuration assignment is only possible if it can be coordinated with the DRX cycle.
  Further handling of DRX may be studied in Release 12.

## Slide 3: Dropped SRS
  Dropped SRS may occur, e.g., due to other channel transmissions.
  Dropped SRS may impact UL RTOA measurement accuracy. That will be analyzed during the performance part of WI.

## Slide 4: UL RTOA Measurement Requirement for TDD
  When Tsrs>2ms, FDD UL RTOA measurement requirements apply also for TDD
  When Tsrs=2ms, the UL RTOA measurement time is as below:

## Slide 5: SRS Configuration Update
  UE SRS configuration may change for one or more cells or the set of cells with SRS configured for the UE may change during UL positioning
  Upon receiving SRS configuration update, the LMU shall continue the UL RTOA measurement for a cell and report the measurement, while meeting the requirements in Section 6, in the following cases:
    the new SRS configuration for the cell is the same as the SRS configuration for this cell before receiving the SRS configuration update
    the new SRS configuration for the cell is a superset of the SRS configuration for this cell received before the update, i.e., the updated SRS configuration comprises the SRS configuration before the update but may also have other SRS configured