## Slide 1: WF on TS 36.111 Section 6 Requirements
TruePosition, Andrew Corporation
3GPP TSG RAN WG4 #67
Fukuoka, Japan, 20-24 April 2013
Agenda Item: 6.8.1.2
R4-132946

## Slide 2: UL RTOA Requirements with DRX
  A UE configured with DRX does not transmit instances of periodic SRS while not in Active Time state [TS 36.321]
  In LTE Rel-11:
    UL RTOA measurements may fail when UE is configured with DRX while the UL RTOA measurements are performed by LMUs
    UL RTOA requirements with DRX are not specified

## Slide 3: UL RTOA Measurement Requirements without DRX
  The currently specified in 36.111 UL RTOA measurement requirements for FDD are limited to when the UE is not configured with DRX
  TDD requirements without DRX
    When Tsrs>2ms, FDD UL RTOA measurement requirements without DRX apply also for TDD
    When Tsrs=2ms, the UL RTOA measurement time is as below:

## Slide 4: Dropped SRS
  With or without DRX, dropped SRS may occur, e.g., due to measurement gaps, autonomous gaps, interruptions due to CA, and other channel transmissions
  UL RTOA measurement performance may degrade when dropped SRS occur

## Slide 5: SRS Configuration Update
  UE SRS configuration may change for one or more cells or the set of cells withSRS configured for the UE may change during UL positioning
  Upon receiving SRS configuration update, the LMU shall continue the UL RTOA measurement for a cell and report the measurement, while meeting the requirements in Section 6, in the following cases:
    the new SRS configuration for the cell is the same as the SRS configuration for this cell before receiving the SRS configuration update
    the new SRS configuration for the cell is a superset of the SRS configuration for this cell received before the update, i.e., the updated SRS configuration comprises the SRS configuration before the update but may also have other SRS configured
    Note: Requirements corresponding to the SRS period before the change apply in both cases above

## Slide 6: 36.133
The agreements in this WF are to be also captured in TS 36.111