## Slide 1: Way forward on BS performance requirements for HSUPA MIMO
Nokia Siemens Networks, QUALCOMM Incorporated, Ericsson, ST-Ericsson
TSG-RAN Working Group 4 (Radio) meeting #67
Fukuoka, Japan, 20 - 24 May, 2013
R4-132966

## Slide 2
Performance requirements of Rel-11 MIMO with 64QAM for HSUPA work item will be completed at RAN4#68
All CRs for performance requirements of Rel-11 MIMO with 64QAM for HSUPA work item will be agreed at RAN4#68

## Slide 3: E-DPDCH/S-E-DPDCH demodulation performance
Correction of FRC10 (S-E-DPCCH/DPCCH power ratio changed from 0dB to 6dB or 8dB) – see Appendix
Simulation results will be provided for FRC9 and FRC10
Interested companies will provide ideal simulation results (with ideal decoding of E-DPCCH and S-E-DPCCH) for alignment as soon as possible
Interested companies will provide realistic simulation results (with realistic decoding of E-DPCCH and S-E-DPCCH) as a baseline for final requirements at RAN4#68

## Slide 4: S-E-DPCCH detection performance
RAN4 has agreed that S-E-DPCCH detection performance requirements are not needed due to introduction of HSUPA MIMO

## Slide 5: TPI generation performance
Introduction of TPI generation performance requirement is subject to testing feasibility
New fixed reference channel defined for TPI generation simulations (FRC11) – see Appendix
Evaluation will be made between fixed beamforming and channel adaptive beamforming
Channel-adaptive beamforming gain will be expressed as throughput gain or as Rx Ec/No gain
Interested companies will provide ideal simulation results (with ideal decoding of E-DPCCH and S-E-DPCCH) for alignment as soon as possible
Interested companies will provide realistic simulation results (with realistic decoding of E-DPCCH and S-E-DPCCH) as a baseline for final requirements at RAN4#68

## Slide 6: Appendix Simulation assumptions
Parameter | Value
Physical channels | DPCCH, S-DPCCH, E-DPCCH, S-E-DPCCH, E-DPDCH and S-E-DPDCH
E-DCH TTI [ms] | 2
Modulation | QPSK, 16-QAM
Channel encoder | 3GPP Release 6 Turbo Encoder
Turbo decoder | Max Log MAP
Number of iterations for turbo decoder | 8
Node B receiver type | Rake and/or LMMSE
Channel estimation | Realistic
Inner loop power control | Off, fixed TX power approach
Outer loop power control | Off
EVM [%] | 0
TX weight vector selection | A fixed precoding weight vector
E-TFC selection | Fixed FRC approach, the same FRC for E-DPDCH and S-E-DPDCH
Propagation channel | Ped A, 3 km/h; Ped B, 3 km/h; Veh A, 3 km/h
Antenna configuration | 2x2
Time Alignment Error at UE | 0Tc
Correlation of channel realizations between TX antennas | 0
Correlation of channel realizations between RX antennas | 0
H-ARQ approach | Incremental redundancy, 4 H-ARQ transmissions at maximum
Metrics | Rx Ec/No at 70% of max throughput

## Slide 7: Appendix FRC9 (boosted E-DPCCH)
Parameter | Unit | Value
Modulation |  | QPSK
Maximum. Inf. Bit Rate | kbps | 8100
TTI | ms | 2
Number of HARQ Processes | Processes | 8
Information Bit Payload (NINF) | Bits | 16200
Binary Channel Bits per TTI (NBIN) (3840 / SF x TTI sum for all channels) | Bits | 23040
Coding Rate (NINF/ NBIN) |  | 0.703
Physical Channel Codes | SF for each physical channel | {2,2,4,4}
E-DPDCH/DPCCH power ratio E-DPCCH/DPCCH power ratio S-DPCCH/DPCCH power ratio S-E-DPCCH/DPCCH power ratio S-E-DPDCH/DPCCH power ratio | dB dB dB dB dB | 6.02 -1.94 -1.94 0.00 6.02 E-DPDCH/DPCCH power ratio is calculated for a single E-DPDCH with SF 4. The power of an E-DPDCH with SF2 is twice that of an E-DPDCH with SF4.

## Slide 8: Appendix FRC10 (boosted E-DPCCH)
Parameter | Unit | Value
Modulation |  | 16QAM
Maximum. Inf. Bit Rate | kbps | 16218
TTI | ms | 2
Number of HARQ Processes | Processes | 8
Information Bit Payload (NINF) | Bits | 32436
Binary Channel Bits per TTI (NBIN) (3840 / SF x TTI sum for all channels) | Bits | 46080
Coding Rate (NINF/ NBIN) |  | 0.704
Physical Channel Codes | SF for each physical channel | {2,2,4,4}
E-DPDCH/DPCCH power ratio E-DPCCH/DPCCH power ratio S-DPCCH/DPCCH power ratio S-E-DPCCH/DPCCH power ratio S-E-DPDCH/DPCCH power ratio | dB dB dB dB dB | 19.99 16.03 16.03 0.00 [6.00] or [8.00] 19.99 E-DPDCH/DPCCH power ratio is calculated for a single E-DPDCH with SF 4. The power of an E-DPDCH with SF2 is twice that of an E-DPDCH with SF4.

## Slide 9: Appendix FRC11 (boosted E-DPCCH)
Parameter | Unit | Value
Modulation |  | 16QAM (E-DPDCH), QPSK (S-E-DPDCH)
Maximum. Inf. Bit Rate | kbps | 12159 (4050 for E-DPDCH and 8109 for S-E-DPDCH)
TTI | ms | 2
Number of HARQ Processes | Processes | 8
Information Bit Payload (NINF) | Bits | 24318
Binary Channel Bits per TTI (NBIN) (3840 / SF x TTI sum for all channels) | Bits | 34560
Coding Rate (NINF/ NBIN) |  | 0.704
Physical Channel Codes | SF for each physical channel | {2,2,4,4}
E-DPDCH/DPCCH power ratio E-DPCCH/DPCCH power ratio S-DPCCH/DPCCH power ratio S-E-DPCCH/DPCCH power ratio S-E-DPDCH/DPCCH power ratio | dB dB dB dB dB | 19.99 16.03 16.03 0.00 [6.00] or [8.00] 19.99 E-DPDCH/DPCCH power ratio is calculated for a single E-DPDCH with SF 4. The power of an E-DPDCH with SF2 is twice that of an E-DPDCH with SF4.