## Slide 1: Way Forward on ON/OFF Model
MediaTek, Orange, Verizon Wireless, Intel, Samsung, Huawei, Qualcomm, Ericsson, LGE, Blackberry, Renesas, Broadcom, NTT DoCoMo
3GPP TSG RAN WG4 #68 R4-134476
Barcelona, Spain, August 19-23, 2013
Agenda item: 10.6.2

## Slide 2: Previous Agreement in Ad-hoc
Interference has a constant MCS/RI across the time and frequency domain for the duration of each packet
Note: This simplified model is adopted for link level evaluation in the study item phase. System level simulation will have realistic interference MCS/RI that varies during each packet, and another model (e.g., Random MCS/RI across subframe and/or subband for the duration of each packet) should be considered for test definition in later Work Item phase, in order to test the robustness of the receivers.

## Slide 3: Working Assumption for the General ON/OFF Model
Packet arrival is a Poisson process with an arrival rate defined as λ= RU / D (mean packet duration from SLS @40% RU, 0.5MBytes)
  RU=40% (for scenario 1), TBD for scenario 2a/2b
  “D” = [250ms] (scenario 1), and for scenario 2a/2b [200ms] (macro interferer) and [100ms] (small cell interferer) [note from DCM R4-133277]
RI=1/2 is randomly chosen according to [50/50] probability [note: from MTK R4-133638 etc.]
MCS varies from packet to packet
  MCS randomly selected from three MCS levels defined below
  RI=2: MCS [5] ([TBD]% prob), MCS[14] ([TBD]%), MCS[19] ([TBD]%)
  RI=1: MCS [8] ([TBD]% prob), MCS[17] ([TBD]%), MCS[22] ([TBD]%)
MCS/RI determines ON duration assuming 0.5MB packets
Values in [] are meant to be a starting point, to be further verified in RAN4