## Slide 1: Way Forward on FeICIC interference estimation under signaling
Qualcomm
R4-134105
3GPP TSG-RAN WG4 Meeting #68
Barcelona, Spain, 19 - 23 August, 2013
Agenda Item: 7.8.2

## Slide 2: Way Forward
FeICIC interference estimation
  In the case of colliding CRS, UE shall perform interference estimation based on the following criteria:
    On subframes indicated by csi-MeasSubframeSet1, UE performs “ABS interference estimation”.
    On other subframes, UE performs “regular interference estimation”, where advanced interference estimation techniques such as blind Nt estimation is not precluded.
  Example
    measSubframePatternPCell is not a trigger for “ABS interference estimation”. measSubframePatternPCell is used simply to enable restricted measurements and improve measurement accuracy via CRS-IC.
Note: CRS interference mitigation could be performed for demodulation enhancements on all subframes.