## Slide 1: Way forward on SU-MIMO for intra-cell scenarios for NAICS
Ericsson, NTT Docomo, Huawei, HiSilicon
R4-135670
TSG RAN WG4 meeting #68bis
Riga, Oct 7-11, 2013

## Slide 2: Background
The current simulation results from all the companies on SU-MIMO intra-cell scenarios for NAICS SI are captured in draft TP R4-134950 .
  The current conclusion is based on results from different setup, eg. OLLA/FRC, HARQ ON/OFF, Rank 2/Follow rank, Different Tx/Rx numbers, Different fading channel correlation and Doppler, etc.
  Only 2 companies provide common setup.

## Slide 3: Way Forward (1/2)
In case time allows the future simulation results should be based on common simulation assumptions.
For interested companies the following simulation assumptions can be taken as common scenarios for the future meetings.
The simulation results should be provided based on practical implementation with complexity considered.

## Slide 4: Way Forward (2/2)
The existing performance requirements are proposed to be reused as followed with certain changes.
  Baseline tests
    Test 1: 36.101 Open loop spatial multiplexing (TM3), Section 8.2.1.3.1
    Test 2: 36.101 Closed loop spatial multiplexing (TM4) Section 8.2.1.4.2
    Test 3: 36.101 Dual-Layer Spatial Multiplexing (TM 9), Section 8.3.1.2
  Optional tests
    Test 1: 36.101 Type A receiver Section 8.2.1.2.4 (TM2/3)
    Test 2: 36.101 Type A receiver Section 8.2.1.4.1B (TM4/6)
    Test 3: 36.101 Type A receiver Section 8.3.1.1A (TM9/9)
  Two sets of results are expected for the tests above with changes as proposed below
  Baseline setup: Current FRC setup with medium correlation, synchronous network
  Optional setup: OLLA with follow CQI and PMI, Rank 2, medium correlation, Doppler 5Hz, synchronous network