## Slide 1: Way Forward on RS-SINR
Qualcomm Incorporated, AT&T, Verizon, NTT Docomo
R4-136909
3GPP TSG-RAN WG4 Meeting # 69
San Francisco, U.S.A. , 11th – 15th November, 2013

## Slide 2: Way Forward
RS-SINR for the serving cell is widely used as a metric to set the antenna bar display in many devices
  RS-SINR is currently not standardized and the antenna bar display can be inconsistent among different devices
RS-SINR for the serving cell will be introduced in the specifications from Rel. 12 (see proposed definition on next page) and measurement accuracy requirements and performance test will be defined
  The proposal is to perform the work under TEI12
  RAN5 test signaling to be used for the test
  Concrete work plan to be agreed in RAN4 #70

## Slide 3: RS-SINR proposed definition
RS-SINR is defined as the linear average over the power contribution (in W) of the resource elements carrying CRS divided by the sum of the noise and interference power contribution (in W) of the resource elements carrying CRS within the considered measurement frequency bandwidth. For RS_SINR determination, the cell-specific reference signals R0 according TS 36.211 shall be used. If the UE can reliably detect that R1 is available it may use R1 in addition to R0 to determine RS-SINR.
The reference point for the RS-SINR shall be the antenna connector of the UE.
If receiver diversity is in use by the UE, the reported value shall not be lower than the corresponding RS-SINR of any of the individual diversity branches