## Slide 1: MIMO OTA WF
Vodafone, Intel, Elektrobit, Motorola Mobility, Spirent, Anite, Docomo, ATR, Agilent, Bluetest, CTTC, Qualcomm
3GPP TSG-RAN WG4 #69 R4-137115
San Francisco, 11th – 15th Nov 2013

## Slide 2: WI conclusions
Test procedures for 4 methodologies: (1) AC multiprobe, (2) RC, (3) RC+CE, (4) 2stage-radiated) out of 8 candidate methodologies: (1) AC multiprobe, (2) RC, (3) RC+CE, (4) 2stage-radiated, (5) AC single cluster, (6) 2stage-conducted, (7) 2-channel, (8) Decomposition) have been validated and specified during WI phase
Out of the 4 validated methodologies:
  Method (1) and method (4) present the same propagation conditions. For AAS capable UE, method (4) requires access to proprietary interface
  Method (4) to be finalized requires UE measurements and test function which specification is out of the scope of this WI
  Methods (2) and (3) present different propagation conditions from methods (1) and (4)
Harmonization has not been feasible by RAN4#69. While there may be potential to harmonize methods, there are also indications that this may not be possible, and so harmonization is uncertain
In order to facilitate a comparison among validated methodologies, main capabilities and limitations are summarized in Clause 12.4 of 37.977 v1.3.0
WI reaches 100% completion level. List of open issues from previous SR approved in RAN#61 in RP-131401 has been completed, and therefore 100% completion is proposed.

## Slide 3: Follow up work
In a potential new WI phase, the following is recommended:
  Develop measurement uncertainty for the methods validated and specified in 37.977 v1.3.0 (Clause 12)
  Development of performance requirements for specific environments that belong to the methodologies that have been validated and specified in 37.977 v1.3.0 (Clause 12)
  After requirements based on an acceptable sufficient range of devices are set, a single and unique set of requirements shall be selected for applicable test conditions, which shall be applicable to at least one methodology
Separate WI may need to be created if validation of additional methodologies not validated and specified in 37.977 v1.3.0 is required. This depends on the work load of this activity