## Slide 1: NAICS RAN1&4 Joint Ad-hoc Discussion on Possible SI Conclusion (For information)
MediaTek
3GPP TSG RAN WG1 Meeting #76
Prague, Czech Republic, 10-14 Feb. 2014
R1-140894

## Slide 2: Background
In the approved status report for the NACIS study item (RP-132108), the following guidance was given for the remaining work:
  Based on RAN#62 discussion, RAN1 and RAN4 should have the following focus and target completion at RAN#63:
    (RAN1) Identify the interference transmission parameters for signalling and those for receiver detection, based on the following studies and the trade-offs:
      Receiver performance and complexity, with and without network assistance (RAN4)
      Feasibility of assistance signalling and system performance that takes into account corresponding signalling overhead (RAN1)
      Network performance evaluation if any network coordination is assumed that introduces scheduling constraints (RAN1).
Previous conclusions captured in TR36.866:
  (RAN1) Compared to requiring NAICS receivers to detect all interference parameters, some network signalling/coordination can be beneficial for reducing receiver complexity and/or improve performance with increased robustness under intra-cell and inter-cell interference scenario.
  (RAN4) Some network assistance/coordination can reduce receiver complexity compared to requiring UE to blindly detect all the interference parameters.
    But there is no consensus on the feasibility and performance of blind detection receivers and it is agreed that RAN4 should study the performance and complexity of blind detection of interference parameters, including which parameters to be blindly estimated by the UEs.
    There was also varying degree of performance degradation from minimal to noticeable depending on operation assumptions, when comparing blind detection receivers with genie-aided receivers.

## Slide 3: Observations and Proposal from Rapporteur
Higher-layer signaling of parameters related to interference PDSCH will be defined in the work item phase because they were found necessary to reduce the blind detection complexity and/or performance degradation.
  See next slides for candidate parameters
For the following parameters of interference PDSCH, some UE blind detection is desirable, possibly detected from a reduced subset (RRC signaled) of all values for some parameters
  Presence or absence of interference
  TM
  For DMRS-based TMs: DMRS ports, modulation order, Virtual cell ID, nSCID
  For CRS-based TMs: PMI, RI, modulation order
  ρA, ρB/ρA
  CFI (if not coordinated and required by receiver implementation)
Blind detection was found acceptable in terms of complexity and with minimal or acceptable degradation in some cases (e.g., for some of the above parameters under some interference conditions), but not in some other cases or at least with inclusive findings. Further study in RAN4 is needed to align observations in the work item phase (e.g., on interference conditions, receiver channel estimation, assumptions on other parameters, reduced subset)
Dynamic signaling from an interference or a serving cell can continue to be evaluated in the work item phase before any RAN4 conclusion on blind detection, but should be under agreeable or comparable conditions and assumptions that include the used physical channel and assumed content.
Conclude the SI with the above conclusions and move to the work item phase

## Slide 4: Candidates for higher-layer signaling
Candidate parameters for higher-layer signaling include
  Any subset restriction on the values for parameters that requires blind detection (see previous slides)
  Resource allocation related parameters
    Granularity (e.g., a group of PRB or PRB pairs)
    RA type (e.g., type 0, LVRB, Ngap used for DVRB)
  Any subset of virtual cell ID (i.e., ) used for TM10
  Cell-ID, CRS ports, and MBSFN pattern (reuse Rel-10 feICIC signaling)
    System bandwidth (if needed)
  Any synchronization indication (e.g., CP length) if needed
  CSI-RS configuration
  QCL

## Slide 5: Next-step for RAN4 (to be discussed)
To align company observations on blind detection complexity and performance, RAN4 to discuss and agree on a set of evaluation conditions such as the following:
  Interference condition
    2 interferers (on/on as defined in phase-1 in RAN4 definition @20%, 50%, 80%)
    Receiver still must detect the presence/absence of interference
  Resource allocation assumed at UE: 1 PRB-pair
  Evaluate the performance of blind detection under the following assumptions (To be discussed, examples only)
    TM (BD)
      TM9-TM9-TM9
      TM9-TM2-TM2
      TM2-TM2-TM2
      TM2-TM9-TM9
      ….
    For DMRS-based TMs: DMRS ports (BD of port 7&8), modulation order (BD), Virtual cell ID (BD from a subset of [..]), nSCID (BD)
    For CRS-based TMs: PMI (BD for 2-Tx), RI (BD), modulation order (BD)
    ρA, ρB/ρA (BD from a subset of [..])
    CFI (BD under misaligned PDSCH starting symbol)
    Cell-ID, CRS ports, and MBSFN pattern (known)
    Any synchronization indication (e.g., CP length) if needed (known and same CP)
    CSI-RS configuration
    QCL

## Slide 6: Possible Conclusions from Joint RAN1&4 Ad-hoc
To reduce the blind detection complexity and/or performance degradation, higher-layer signaling of some parameters (including subset restriction) can be defined (without precluding blind detection) after identifying those parameters
Dynamic signaling can be considered if blind detection with higher-layer signaling is not acceptable in terms of performance degradation and/or receiver complexity