## Slide 1: Proposed test for DL CA with 2 or 3DL CCs with minimum channel spacing in Rel-12
Agenda Item: 7.42.1
Document for: Approval
Source: Ericsson
3GPP TSG-RAN WG4 Meeting #70bis R4-142066
San Jose Cabo, Mexico, 31 Mar-4 Apr, 2014

## Slide 2: Background
With CA in 3DL CCs on Band 41 a minimum channel spacing is proposed.
  Instead of the nominal channel spacing a minimum spacing as 18.3MHz will be used in intra-band contiguous CA on Band 41 to match operator allocations.
In order to make proper conformance test with this minimum spacing configuration some extra performance tests would be needed to verify functionality at minimum carrier spacing.

## Slide 3: Discussion on test purpose
Rather than specifying an RF test with a wanted signal near the sensitivity level and with a low code rate, we propose to verify functionality by a performance test with the standard external interference level.
As with smaller channel spacing the ACI (adjacent channel interference) could be more crucial under high SNR conditions so the tests should use a high code rate like 64QAM to end up at a SNR level in 18~20dB. And the test should be band agnostic but only apply to CA configuration with minimum channel spacing.

## Slide 4: Proposed test scenario
Proposal : Define extra performance tests applied to CA configuration with minimum channel spacing for 2 or 3 DL CCs eg. TM1 FRC test with 64QAM and code rate ¾.
  Tests only applied to CA configuration with minimum channel spacing
  Band agnostic tests in Rel-12
  1 test for 2 CCs with bandwidth combination as 20+20MHz
  1 test for 3 CCs with bandwidth combination as 20+20+20MHz
  TM1, EVA5, R.9 FDD