## Slide 1: 3DL CA relaxations
Broadcom Corporation
3GPP RAN4 meeting #70bis
San Jose del Cabo, Mexico, March 31 – April 04, 2014
R4-142504
Document for: Discussion

## Slide 2: Open issues
Disagreement with current WF
LLL and HHH relaxations
Multiple 3DL CA combination relaxations

## Slide 3: Disagreement with current WF
Relates to derivation of the relaxations for LLH and LHH in case when UE supports one 3DL CA combination
With ever increasing complexity some changes seem inevitable to reach an agreement for multiple 3DL CA combinations
An alternative to Ericsson/Qualcomm proposals might be to set upper bound for the difference (approach explained in BRCM paper).

## Slide 4: LLL and HHH relaxations
Use additional insertion loss of a LLL component (likely Hexaplexer) to define ΔTIB, ΔRIB
  Shared pain approach
Use additional insertion loss of a HHH component (quadplexer+diplexer, 2 diplexers, hexaplexer) to define ΔTIB, ΔRIB
  Shared pain approach

## Slide 5: Multiple 3DL CA combination relaxations
For both low and high bands, apply the maximum relaxation for each band among the supported 2DL and 3DL CA combinations