## Slide 1
3GPP TSG-RAN WG4 Meeting#70bis R4-142541
San Jose del Cabo, Mexico, 31 March - 4 April 2014
Agenda item: 5.7
Source: KDDI
Document for: Approval
Title: Way Forward on PUCCH overprovisioning requirement for Band 28 spectra

## Slide 2: Background
Band 28 terminal comprises dual duplexers, which are called as Lower and Higher DUP, respectively.
Operator A in Figure 1 can utilize both duplexers from perspective of spectrum allocation.
PUCCH overprovisioning is required for Lower DUP operation to meet co-existence requirement with DTV.
Figure 1: Band 28 duplexer arrangement

## Slide 3: Contributions for RAN4#70-bis
Following contributions were submitted with significant simulation results.
  R4-141294: Qualcomm Incorporated
  R4-141795: Huawei, Hisilicon
  R4-141975: Nokia Corporation
  R4-142006: Intel Corporation
  R4-142051: Ericsson
  R4-142116: Broadcom Corporation
  R4-142228: Motorola Mobility

## Slide 4: Case#1: 5MHz CBW
On 5MHz CBW operation within UL/DL = 718-728/773-783 MHz, no company reports that PUCCH overprovisioning or RB restriction is needed.
Proposal#1: No restriction is required for achieving DTV co-existence requirement on 5MHz CBW operation within UL/DL = 718-728/773-783 MHz.

## Slide 5: Case#2-1: 10MHz CBW PUCCH overprovisioning
One company reports no PUCCH shift is required.
Five companies indicate 1RB shift is required.
One company reports that 7RB shift is needed.
  After offline discussion, it is clarified that not 7RB but 2RB shift is enough to meet DTV requirement.
Proposal#2-1: For PUCCH overprovisioning, 2RB shift for both sides is required for
achieving DTV requirement.

## Slide 6: Case#2-2: 10MHz CBW maximum number of contiguous RBs
One company reports 26RBs.
Results in another one company shows 27RBs.
30RBs and 36RBs are recommended by two companies, respectively.
One report says 40 RBs is possible.
Proposal#2-2: For maximum number of contiguous RBs, one value between 26~40 would be taken to specify.

## Slide 7: How to specify into TS36.101
Recommendation in R4-142051 is appropriate because it is consistent approach with Band 8 operation in Japan.
Proposal#3: Baseline of how to specify into TS36.101 should follow proposal in R4-142051.
E-UTRA Band | Spurious emission |  |  |  |  |  | 
 | Protected band | Frequency range (MHz) |  |  | Maximum Level (dBm) | MBW (MHz) | Note
28 | … |  |  |  |  |  | 
 | Frequency range | 470 | - | 710 | -26.2 | 6 | X
NOTE X: This requirement is applicable for 5 and 10 MHz E-UTRA channel bandwidth allocated within 718-728MHz. For carriers of 5 MHz bandwidth, no restriction on uplink transmission is required. For carriers of 10 MHz bandwidth, this requirement applies for an uplink transmission bandwidth less than [X] RB with [RBstart >1] and [RBstart < 48]. |  |  |  |  |  |  |