## Slide 1: Way forward on demodulation test under high Doppler EVA600 scenario
NTT DOCOMO, INC., Huawei, Intel, Ericsson
R4-145395
3GPP TSG-RAN WG4 Meeting #72
Dresden, Germany, 18 Aug – 22 Aug 2014

## Slide 2: Background
Based on the evaluation of PDCCH performance in [2], it was confirmed that
  PDCCH performance of some chipset degrades in EVA600 scenario.
  Especially, when the aggregation level is lower, the larger numbers of poor performance UEs were observed. And thus the PDCCH performance of some chipsets are not guaranteed in a very low aggregation level.
In addition to the degradation of PDSCH performance found at last RAN4#71 meeting[1], it can be concluded that both PDSCH and PDCCH performance of some chipset degrades seriously in EVA600 case.
Given the fact that there were two channels degraded according to the investigation, the same situation may also happen in other channels such as PHICH, PCFICH and PBCH.
Notes: E///, CMCC, Intel, NVDIA,

## Slide 3: Way forward
We encourage companies to further investigate PHICH, PCFICH and PBCH performance with EVA600 scenario.
  Evaluation of PCFICH, PHICH, and PBCH can be considered based on test cases in Table 1, Table 2, and Table3, respectively.
    Other scenarios are not excluded.
  For the comparison, propagation condition can be appropriately replaced by EVA70, EVA200, etc., while it can be reused for the other parameters .

## Slide 4
Test number | Bandwidth | Aggregation level | Reference Channel | OCNG Pattern | Propagation Condition | Antenna configuration and Correlation Matrix | SNR (dB)
1 | 10 MHz | 8 CCE | R.15 FDD | OP.1 FDD | EVA600 | 1x2 Low | -1.7
2 | 10 MHz | 4 CCE | R.16 FDD | OP.1 FDD | EVA600 | 2 x 2 Low | -0.6
3 | 5 MHz | 2 CCE | R.17 FDD | OP.1 FDD | EVA600 | 4 x 2 Medium | 6.3
Table 1: Evaluation Conditions of PCFICH
Test number | Bandwidth | Reference Channel | OCNG Pattern | Propagation Condition | Antenna configuration and Correlation Matrix | SNR (dB)
1 | 10 MHz | R.18 | OP.1 FDD | EVA600 | 1 x 2 Low | 5.5
3 | 10 MHz | R.19 | OP.1 FDD | EVA600 | 2 x 2 Low | 4.4
5 | 5 MHz | R.20 | OP.1 FDD | EVA600 | 4 x 2 Medium | 6.1
Table 2: Evaluation Conditions of PHICH

## Slide 5
Test number | Bandwidth | Reference Channel | Propagation Condition | Antenna configuration and Correlation Matrix | SNR (dB)
1 | 1.4 MHz | R.21 | EVA600 | 1 x 2 Low | -6.1
2 | 1.4 MHz | R.22 | EVA600 | 2 x 2 Low | -4.8
3 | 1.4 MHz | R.23 | EVA600 | 4 x 2 Medium | -3.5
Table 3: Evaluation Conditions of PBCH

## Slide 6: References
[1] R4-142884, “Discussion on scope of demodulation test under high Doppler environment” , NTT DOCOMO, TSG-RAN WG4 Meeting #71, Seoul, Korea, May 19 – 23, 2014
[2] R4-144399, “Further discussion on demodulation test under high Doppler environment” , NTT DOCOMO, TSG-RAN WG4 Meeting #72, Dresden, Germany, Aug 18 – 22, 2014