## Slide 1: 1+28 and 7+8 Way Forward
[Vodafone]
RAN4 #72 Dresden R4-145554
Vodafone
Approval

## Slide 2: Background: from ad-hoc meeting minutes in R4-14XXXX
It has been proposed to use trap filter (TF) within shared pain approach
Several understandings on
  the IL of trap filter
  and shared pain approach
Chair summary: For at least low and high A2 band combinations (not considering very high bands, B42),
 | ∆T | ∆R | Comments
Qualcomm | T=0.3 (DPX)+0.3 (TF)=0.6 | 0.3 (TF) | Based on 0.6 average IL for TF
Ericsson | 0.5 | 0 | 
Vodafone | 0.5 | 0 | 
KDDI | 0.5 | 0.2 | which would make it more acceptable, compromise, for those operators who don’t need trap filter
 | ∆T | ∆R
Low band | 0.5dB | 0->0.3dB
Notes: DeltaT
Chair: looking at data, is 0.5dB more acceptable ¡n delta T?
QCM: is the IL or relaxation the problem?
VF: relaxation is what matters
Docomo: what is the attenuation of the harmonic filter?
KDDI: att is 30dB if remember correctly
QCM: att in what freq?
Docomo: at victim Rx band. IL depends on freq and att.
QCM: IL also varies across pass band. We have to check the details
Docomo: not good approach. Our concern is high freq. that same relaxation will be applied 3+42. so it should be case by case
QCM: disagree. Considering that we have many combinations we have to simplify. When we agreed A1s that was successful.
TIM: our preference is case by case. What is the variability of these values (0.5dB) across bands?
QCM: the diff 700-900 is 0.1dB
KDDI: regarding optimization, we agree with QCM. Optimization is implementation phase. This is min requirements
Chair: would it be acceptable to assume 0.5dB for delta T considering the affected band is <1Ghz band?
QCM: no band >1GH is affected
Nokia: 3+42 has a problem
QCM: ok. 0.5dB can be ok if we look at the package in deltaR
DeltaR:
Chair: as refsens is easier. 0.3 is not acceptable. 0 seems not either. Then, is it acceptable 0.1?
QCM: if total loss is about 1.1 or 1.2dB, then the pain should be around 1dB, which seems excessive
TIM: ref sens margins are huge.
QCM: we disagree
KDDI: also ok to 0.2. we cannot understand diff betwee 0.1 and 0.2
Telecom Italia: it is said total loss 1.1dB, but in deltaT was 0.5. there is a difference from 0.7
Chari: Other companies onjsecting to 0.2?
Orange: cocern on ref sens
KT: 0.2 seems best compromise
QCM: share pain in ref sense is more than 50/50
QCM: the threshold seems to be less than 0.2dB in ref sens. We think operators are not willing to accept harmonic trap filter
Chair: delta T seems to be ok on 0.5dB. DeltaR is between 0.1 or 0.2dB
KT:
Chair summary:
For at least low and high A2 band combinations (not considering very high bands, B42),
deltaT: 0.5dB
deltaR: 0->0.3dB

## Slide 3: Way Forward
The following is agreed
  Trap filter is initially assumed for A2 combination involving <1GHz band and >1GHz (i.e. excluding in principle very high bands 3+42)
  Relaxations in deltaT and deltaR as follows
  MSD 1+28
  MSD 7+8
 | ∆T | ∆R
Low band | 0.5dB | 0.2dB
Band 1 CBW | 5MHz |  | 10MHz | 15MHz | 20MHz
AVERAGE | MSD Refsens | 8.6 -91.4 | 6.2 -90.8 | 5 -90.2 | 4.3 -89.7
Band 7 CBW | 10MHz |  | 15MHz | 20MHz
AVERAGE | MSD Refsens | 6 -89 | 4.8 -88.4 | 4.03 -88