## Slide 1: Proposed formatting of new CA combinations WIDs
Qualcomm Incorporated
3GPP TSG-RAN4#72 R4-145097
Dresden, Germany, August 18th – 22nd, 2014
Document for: Discussion
Agenda Item: 11

## Slide 2: Problem statement
Carrier aggregations scenarios are becoming more complex
  1UL/2DL, 2UL/2DL, 1UL/3DL, 1UL/4DL, 1UL/5DL, etc
  FDD + TDD
  Contiguous, non-contiguous, and hybrids
  Inter-band, intra-band, and hybrids
  SDL and SUL
UL and DL CA configurations should be coupled since they are not treated independently in RAN4
  A particular CA combination is 1UL/2DL for example, which would not include 2UL/2DL for the same bands
Bandwidths and bandwidth combination sets
WID’s are not written in a consistent manner, making it more difficult to interpret
Fallback modes

## Slide 3: Proposal
Include in the WID the CA configuration, not just the bands to be combined
  For example, CA_41A-41C or CA_2A-4A-13A
    The nomenclature is explained in Appendix
  Note that ordering is significant
    Band numbers are in numerical order
    Band class within a band indicates CC’s in increasing frequency. For example, CA_41A-41C is different from CA_41C-41A.
Uplink designation
  Each DL CA configuration should be paired to an UL CA configuration
  For example, CA_2A-4A-13A is specified as single UL only. It should be clear if this single uplink is in any of Band 2, Band 4, and Band 13, or only in some subset. For example, CA_1A-41C only allows single carrier uplink in Band 1.
  Another example, CA_41A-41C DL paired to CA_41C UL (2UL/3DL)
Bandwidths
  Ordering is significant, indicating the order of CC’s from lower frequency to higher frequency. 25+50 RB is different from 50+25 RB for contiguous intra-band CA.
Fall back modes
  All fallback modes which are currently not already defined in the specification should be included as part of the WI
  Fall back combinations should also follow all of the above guidelines

## Slide 4: Suggested template
TBD