## Slide 1: Proposed formatting of new CA combinations WIDs
Qualcomm Incorporated
3GPP TSG-RAN4#72bis R4-146483
Singapore, SG, October 6th – 11th, 2014
Document for: Discussion
Agenda Item: 11

## Slide 2: Problem statement
Carrier aggregations scenarios are becoming more complex
  1UL/2DL, 2UL/2DL, 1UL/3DL, 1UL/4DL, 1UL/5DL, etc
  FDD + TDD
  Contiguous, non-contiguous, and hybrids
  Inter-band, intra-band, and hybrids
  SDL and SUL
UL and DL CA configurations should be coupled since they are not treated independently in RAN4
  A particular CA combination is 1UL/2DL for example, which would not include 2UL/2DL for the same bands
Bandwidths and bandwidth combination sets
WID’s are not written in a consistent manner, making it more difficult to interpret
Fallback modes
It is not possible by reading the WI acronym to know what type of CA it is

## Slide 3: WI Acronym
Tradeoff between complexity in the acronym and the amount of information it provides
  Propose to include CA configuration as part of the acronym
  Propose to include number of UL and DL CC’s
  Propose to indicate whether the WI is only introducing new bandwidth combination sets
Examples: “CA_25A-41C_1UL2DL” or “CA_25A-41C_2UL2DL” or “CA_12B_BCS”
  Another possibility: Revert the previous agreement that addition of new bandwidth combination sets requires a new WI

## Slide 4: WID Required information
The bands and CA classes
  CA classes indicate number of CC’s and contiguous vs. non-contiguous
  For NC, does ordering matter? Presently, no. There is presently no significance between for example CA_xA-xC and CA_xC-xA.
Uplink and downlink
  Uplink CA configurations must be a subset of downlink CA configurations.
  UL and DL CA configurations must be linked together, even though RAN2 signaling allows them to be independent
  For each DL CA configuration, not all possible UL CA configurations will be defined unless listed in the work item
    Ex 1: DL = CA_xA-yC, UL = CA_xA or CA_yA. Note that the for uplink in Band y, the single carrier can be in either of the two contiguous carriers of the downlink
    Ex 2: DL = CA_xA-yC, UL = CA_xA only
    Ex 3: DL = CA_xA-xC, UL = CA_xA only (There is presently no way to distinguish which CC that uplink goes on, it could be any of the three. There may be benefit in allowing such a distinction)

## Slide 5: WID Required information (cont)
Bandwidths and bandwidth combination sets
  For each CA configuration, one or more bandwidth combination sets must be defined
  For each CC within a CA configuration, bandwidths must be defined. The set of bandwidths for all CC’s within the CA configuration is the bandwidth combination set.
  Bandwidths and bandwidth combinations sets must be the same for both UL and DL CA
Fallback modes
  If the fallback mode is not already defined in the spec, or part of another work item, then it should be included in this work item
  For all fallback modes, the required information must also be provided.
  For ease of finding, maybe these should be in separate work items? At the present, fallback mode band combinations are “hidden”

## Slide 6: Proposed format
See attached document for examples

## Slide 7: Potential signaling changes for consideration
The following would likely require changes to current RAN2 signaling
  Introduce significance in ordering of NC intra-band sub-blocks, i.e., CA_xA-xC vs. CA_xC-xA, or CA_xA-xC-xA vs. CA_xA-xA-xC
    Might give opportunity to optimize refsens spec, for example if A uplink is closer to C downlink.
    Benefit seems marginal, not recommended.

## Slide 8: Potential signaling changes for consideration (cont)
  Introduce ability to signal the specific pairing between UL and DL CC’s
    For example, for DL: CA_xA-xC, UL:CA_xA, the uplink could be in any of the three CC’s.
    However, there may be benefit to limiting the uplink to the A sub-block to reduce hardware requirements for TDD (Tx and Rx LO’s)
If only 2 LO’s are available, the
UL in the A block can be supported, but not the UL in C block.
If there is no signaling distinction, then with 2 LO’s available, UL CA cannot be supported at all.

## Slide 9: Potential signaling changes for consideration (cont)
  Since UL and DL are not independent, is it possible to add new UL configurations to a CA configuration that has already been completed?
    For example, CA_xA-yC already completed with CA_xA allowed as DL
    Later, it is desired to add single uplink in Band y as well. Or 2UL CA_yC? Or 2UL CA_xA-yA?
    In general, it may not be possible. A new CA configuration would have to be defined, but not possible to distinguish different configurations in current signaling.

## Slide 10: Reporting
Which TR should it go into?
  Rel-13 Inter-band 1UL/2DL TR (class A1-A5) – Ericsson
  Rel-13 Inter-band 2UL/2DL TR (class A1-A5) – Huawei
  Rel-13 Inter-band 1UL/3DL TR – ZTE
  Rel-13 Inter-band 1UL/4DL TR – Nokia
  Intra-band combinations have standalone TR’s
What about others?
  FDD+TDD CA
    Can be handled as part of inter-band TR’s
  Inter-band + Intra-band CA? (with one or more UL)
  Intra-band NC + C? (with one or more UL)