## Slide 1
3GPP TSG-RAN WG4 Meeting#72bis R4-145820 Singapore, 5th – 10th October, 2014
Agenda item: 7.25.1
Source: KDDI
Document for: Approval
Title: Way Forward on MSD for CA_B1_B28

## Slide 2: MSD requirements
Given that situation in certain region is unclear, most of parties prefer flexibility.
  Requirements for UEs with HTF
  Requirements for UEs without HTF
 How to capture in TS36.101?

## Slide 3: Proposal (i)
Specify relaxed values in MSD table. This implies values for UEs without HTF.
* Values from proposal in R4-146385.
Channel bandwidth |  |  |  |  |  |  |  | 
EUTRA CA Configuration | EUTRA band | 1.4 MHz (dBm) | 3 MHz (dBm) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | Duplex mode
CA_1A-28A | 1 |  |  | -81.6 | -81.6 | -81.5 | -81.5 | FDD
 | 28 |  |  | -98.5 | -95.5 | -93.7 | -91 | 

## Slide 4: Proposal (ii)
Make informative annex in TS36.101. This implies values for UEs with HTF.
* Values from proposal in R4-146492.
Channel bandwidth |  |  |  |  |  |  |  | 
EUTRA CA Configuration | EUTRA band | 1.4 MHz (dBm) | 3 MHz (dBm) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | Duplex mode
CA_1A-28A | 1 |  |  | -89.8 | -89.4 | -89 | -88.7 | FDD
 | 28 |  |  | -98.5 | -95.5 | -93.7 | -91 | 

## Slide 5: Signaling
This is out of scope in this contribution because it relates to generic class A2 topic.