## Slide 1: WF for D2D RRM
Ericsson
R4-146676
3GPP TSG-RAN WG4 Meeting #72bis
Singapore, Oct. 6th – Oct. 10th, 2014

## Slide 2: Requirements for UEs in RRC_IDLE
PCell interruption requirements due to switching reception between D2D-to-WAN or WAN-to-D2D needs be defined in RRC IDLE state.
UE capable of D2D discovery and D2D communication in RRC_IDLE state is allowed to interrupt PCell in UL and DL on 1 subframe during the RRC reconfiguration procedure that includes the configuration message proseDiscConfig or proseCommConfig

## Slide 3: Requirements for UEs in RRC_IDLE cont.
The D2D capable UE shall prioritize the monitoring of paging reception and acquisition of SI (MIB, SIBs) over reception of discovery signals in case both occur simultaneously.

## Slide 4: Requirements for UEs in RRC_CONNECCTED
The requirements shall apply when the D2D capable UE is configured with only PCell
PCell interruption requirements due to switching reception between D2D-to-WAN or WAN-to-D2D also needs be defined RRC CONNECTED state.
  UE capable of D2D discovery and D2D communication in RRC_CONNECTED state is allowed to interrupt PCell in UL and DL on 1 subframe during the RRC reconfiguration procedure that includes the configuration message proseDiscConfig or proseCommConfig
      Additional PCell interruption of 1 ms due to switching reception between D2D and WAN subframes is allowed for D2D Discovery capable UE

## Slide 5: Requirements for UEs in RRC_CONNECCTED cont.
The D2D capable UE shall prioritize the WAN measurement procedure over D2D operation.
For the following WAN measurements additional clarification is needed
  At least one cellular DL subframe, subframe 0 or 5, is available in every radio frame for cell identification purpose.
  UE Rx-Tx time difference measurement requirement shall apply provided at least one UL WAN subframe per radio frame is available at the UE over L1 measurement period.
  The D2D capable UE shall prioritize the WAN measurement reporting over D2D operation.
    Due to D2D operation an additional delay in WAN measurement reporting can be expected.
  The D2D capable UE when configured with WAN measurement gaps:
    UE shall not perform D2D operation in the gaps while performing the WAN measurements during the gaps
    UE is allowed to perform D2D operation in the gaps when the gaps are not used for the WAN measurement.

## Slide 6: Requirements for UEs in OoC
Requirements in OoC are FFS subject to RAN1 agreement

## Slide 7: D2D UE Tx timing
RRC_IDLE
  D2D capable UE for D2D transmission shall use eNB DL timing
RRC_CONNECTED
  D2D capable UE for D2D transmission shall use eNB DL timing provided valid Timing Advance (TA) is not available
    If DL timing is used, requirement as specified for PRACH shall apply
  D2D capable UE for D2D transmission shall use TA for UL timing provided valid TA is available
    If UL timing is used, requirement as specified for PUSCH shall apply
OoC
  Timing is FFS subject to RAN1

## Slide 8: Interruption in DRX in RRC_CONNECTED
No PCell interruption due to D2D operation allowed when D2D UE is configured in DRX mode.
  D2D operation can be performed during DRX-OFF duration

## Slide 9: Where to capture the requirements…
Requirements shall be defined for UEs in each state
  RRC_IDLE, RRC_CONNECTED, Out-of-Coverage
All new D2D RRM requirements are specified in a separate clause of the relevant requirements group section in TS 36.133, e.g.:
  D2D requirements for UEs in RRC_IDLE in a new clause 4.4,
  D2D measurement requirements for UEs in RRC_CONNECTED in a new clause 8.X (i.e. one available after 8.4),
  D2D measurement accuracy requirements for UEs in RRC_CONNECTED in a new clause 9.7,
  All D2D requirements in out-of-coverage in a new section 11.
Cellular requirements for D2D-capable UEs are specified in a separate subclause of the relevant cellular requirements section in TS 36.133.