## Slide 1: Way Forward on RLM Requirements for LC-MTC
Ericsson, Huawei, HiSilicon, Vodafone, Verizon
R4-147434
3GPP TSG-RAN WG4 Meeting #73
San Francisco, USA, 17th Nov – 21th Nov. 2014

## Slide 2: Background
In RAN4, the PDCCH RE power boost for LC-MTC RLM and the LC-MTC RLM evaluation period have been discussed for several meetings, no consensus is achieved.
  The majority companies agree to have PDCCH RE power boost for LC-MTC RLM, which is captured in R4-71AH-0087 and endorsed by RAN4#71Adhoc meeting.

## Slide 3: Wayforward
The following PDCCH/PCFICH parameters may be selected for LC-MTC RLM setup:
    For OOS, the ratio of PDCCH RE energy to average RS RE energy is:
      [4] dB; when single antenna port is used for cell-specific reference signal transmission by the PCell (no change to current setup for legacy UE)
      [4] dB; when two or four antenna ports are used for cell-specific reference signal transmission by the PCell.

## Slide 4: Wayforward
  For INS, the ratio of PDCCH RE energy to average RS RE energy is:
    when single antenna port is used for cell-specific reference signal transmission by the Pcell
      [1] dB
    When two or four antenna ports are used for cell-specific reference signal transmission by the Pcell
      [1] dB
  Both for OOS and INS, the “Ratio of PCFICH RE energy to average RS RE energy” of legacy UE is reused.