## Slide 1: WF on simulation assumptions for D2D REFSENS demodulation
Qualcomm Incorporated, Intel
R4-148062
3GPP TSG-RAN WG4 Meeting #73
San Francisco, Nov. 17th – Nov. 21st, 2014

## Slide 2: Background
RMC for D2D REFSENS were agreed in RF room as captured in TR 36.843 v0.2.0 [R4-146963] and updates agreed this meeting [R4-146973]
RMC for D2D Discovery
  On last Editor’s note above, RAN1 agreement from this meeting (RAN1#79, Chairman’s Notes)
Parameter | Unit | Value |  |  |  |  | 
Channel bandwidth | MHz | 1.4 | 3 | 5 | 10 | 15 | 20
Allocated resource blocks |  |  |  | [2] | [2] | [2] | [2]
Subcarriers per resource block |  |  |  | 12 | [12] | [12] | [12]
Allocated subframes per Discovery period |  |  |  | [1] | [1] | [1] | [1]
Modulation |  |  |  | QPSK | QPSK | QPSK | QPSK
Transport Block Size |  |  |  | [224] | [224] | [224] | [224]
Transport block CRC | Bits |  |  | [24] | [24] | [24] | [24]
Maximum number of HARQ transmissions |  |  |  | [1] | [1] | [1] | [1]
Binary Channel Bits | Bits |  |  | [576] | [576] | [576] | [576]
Max. Throughput averaged over 1 Discovery period | kbps |  |  | [TBD] | [TBD] | [TBD] | [TBD]
UE Category |  |  |  | [≥ 1] | [≥ 1] | [≥ 1] | [≥ 1]
Note 1: For PSDCH transmission, the last symbol shall be punctured as per TS 36.211. Editor’s Note: Throughput (in kbps) will depend on discovery period configuration. Editor’s Note: Further details for specifications will be required (e.g., discovery pool configuration, etc.). However, the above details are sufficient to simulate the RMCs. Editor’s Note: TBS size may increase by 1 byte due to additional 4 bits in discovery message requested by SA3 [S3-142355]. |  |  |  |  |  |  | 
Table 9.1-1: D2D discovery reference measurement channel for receiver requirements (FDD)
Agreements:
Discovery message size (excluding the CRC) should be increased to 232 bits.

## Slide 3: Background
RMC for D2D Communications
Parameter | Unit | Value |  |  |  |  | 
Channel bandwidth | MHz | 1.4 | 3 | 5 | 10 | 15 | 20
Allocated resource blocks |  |  |  | [25] | [50] |  | 
Subcarriers per resource block |  |  |  | 12 | 12 |  | 
Packets per SA period |  |  |  | [TBD] | [TBD] |  | 
Modulation |  |  |  | [QPSK] | [QPSK] |  | 
Transport Block Size |  |  |  | [2216] | [4392] |  | 
Transport block CRC | Bits |  |  | [24] | [24] |  | 
Maximum number of HARQ transmissions |  |  |  | [4] | [4] |  | 
Binary Channel Bits | Bits |  |  | [7200] | [14400] |  | 
Max. Throughput averaged over 1 SA period | kbps |  |  | [TBD] | [TBD] |  | 
UE Category |  |  |  | [≥ 1] | [≥ 1] |  | 
Note 1: For PSSCH transmission, the last symbol shall be punctured as per TS 36.211. Editor’s Note: Throughput (in kbps) will depend on discovery period configuration. Editor’s Note: Further details for specifications will be required (e.g., SA and data pool configuration, etc.). However, the above details are sufficient to simulate the RMCs. |  |  |  |  |  |  | 
Table 6: D2D communications reference measurement channel for receiver requirements (FDD)

## Slide 4: Proposed simulation assumption
Only applicable to RMCs for D2D REFSENS for the purpose SNR derivation of REFSENS requirement
  The details of the parameters in square brackets above can be discussed over email prior to the next meeting to align the simulation assumptions and results.
D2D Test/Simulation parameter | Proposals
 | Rx RF characteristics
AGC settling time (not used for demodulation) | QPSK: 1 symbol
Tx EVM | 10%
UE RRC state | Not required for simulation purpose. Will be needed when test procedure is defined, and is FFS
Propagation channel | Static H = [ 1; 1]
Doppler spectrum | N/A
Timing error (eNodeB DL and D2D Tx) | [±12Ts]
Frequency error (eNodeB UL and D2D Tx) | ±10 Hz, Optional ±200Hz
HARQ retransmissions | Discovery: 0 Communications: 3
Soft-combining | No soft combining for Discovery 1 Communiction: Option 1: No soft combining Option 2: Use sof combining Note: Joint-channel estimation over HARQ retransmission is not performed.
Performance metric | SNR @ x% [BLER]/[Throughput]