## Slide 1: WF on harmonic filter handling on CA_3A-42A and CA_3A-42C
NTT DOCOMO, INC.
R4-147285
3GPP TSG-RAN WG4 Meeting #73
San Francisco, 17th to 21th, November 2014

## Slide 2: Background
Mainly the following aspects were discussed in the AH meeting (R4-148024).
The trade-off
  Between MSD values for B42 and DTIB and DRIB for B3
    Smaller MSD becomes, larger the DTIB and DRIB become
      Smaller MSD becomes, larger both PCB isolation and filter attenuation become
      Without large attenuation and DTIB and DRIB , large PCB isolation isn’t useful
  With or without harmonic trap filter(HTF) and its position
MSD
  MSD for channels where 2nd harmonic (H2) directly hits and does not hit.

## Slide 3: Way forward(1)
Companies are encouraged to study MSD with harmonic trap filter(HTF) and without HTF.
  With HTF, the following two positions of it should be considered.
    Between PA and Duplexer and between Duplexer and switch
  If the HTF is introduced, 0.6 dB for DTIB and 0.2 dB for DRIB

## Slide 4: Way forward(2)
Channel conditions for MSD study
3400 MHz
3600 MHz
MSD B
20 MHz CBW
15 MHz CBW
10 MHz CBW
5 MHz CBW
Channel where 2nd harmonic directly hits. They are 5, 10, 15 and 20 MHz
Offset: [10] MHz
Channels where 2nd harmonic does not directly hits.
MSD A
MSD B

## Slide 5: Way forward(3)
The following MSDs are evaluated.
  MSD A:
    The MSDs for channels where H2 directly hits are applicable to the adjacent [10] MHz offset regions as well.
  MSD B:
    The MSDs with [10] MHz offset:
Baseline of the conditions to derive MSD A and B
  Filter attenuation on the assumption that DTIB and DRIB are 0.6 and 0.2 dB, respectively.
  Using other parameters on the assumption that the MSD B for 20 MHz channel bandwidth is [0] dB.
  Any other additional considerations are not precluded.