## Slide 1
3GPP TSG-RAN Working Group 4 Meeting #74 R4-150538
Athens, Greece, 9-13 February 2015
Source: Nokia Corporation, Ericsson, CMCC
Title: Way forward on Pairing UL and DL CA configurations
Agenda item: 3.1
Document for: Approval
___________________________________________________________________________
Background:
For DL carrier aggregation perspective, in Rel-12, some 3DL CA configurations were completed at RAN#66 (December 2014) In the market, 3DL CA service was launched in the end of 2014.
For UL carrier aggregation perspective, 2UL CA features were completed in Rel-12 time frame. Moreover, some 2UL CA configurations like 1+3, 1+19 and 3+19 are constituent 2DL CA configurations for 3DL CA like 1+3+19. Therefore, it would be natural that 3DL CA of 1+3+19 and 2UL CA of 1+3, 1+19 and 3+19 can be used in the same network.
With the consideration of the above it is important that the requirements for 2UL/3DL CA should be specified as soon as possible.
REFERENCE: R4-73AH-0034: Handling of inter band CA for 2UL/3DL for FDD, Source: NTT DOCOMO, INC.

## Slide 2
Way Forward
Start a common WI in next RAN#67 for pairing of existing interband 3 DL CC (3 bands) and 2 UL CC (2 bands) CA configurations.
Scope of the work
As a part of the WI evaluate the impact of the active 2UL CCs on DL CC whose UL is not active for individual inter band CA configurations and agree how the Rx requirements are defined. Enhance current 2UL Class A4 MSD requirement table to cover cases where band other than the ones transmitting is interfered or create new table for this.
Technical report and CR handling
One Technica report is used to document the studies for all 3DL/2UL pairs and for general aspects such as how Rx requirements are defined
Once the work for at least one 3DL/2UL CA configuration pair is complete and the way how to define Rx requirements is agreed a CR for TS36.101 is created.
A common CR covering new 3DL/2UL CA configuration pairs that are finalized is agreed in RAN4 prior each RAN Plenary to ensure that there is no delay introducing requirements into the specifications.

## Slide 3
WI project management
3DL/2UL configuration pairs part of the WI are proposed by operators and captured into the WID by the rapporteur.
Only such 3DL and 2UL CA configurations can be part of the WI which are already specified in TS 36.101.
New 3DL/2UL CA configuration pairs can be proposed until end of REL-13 and WID is updated to include those.
Finalized 3DL/2UL CA configuration pairs are listed as completed 3DL/2UL pairings in the WID.
Those 3DL/2UL CA configuration pairs that are not completed during REL-13 will be part of REL-14 work
Further details
For DL CA configuration A+B+C It is not mandatory to specify pairing for all three 2 UL combinations A+B, B+C and A+C if not defined in the WID.
In Athens we discuss
For DL CA configuration A+B+C In case all three 2 UL combinations A+B, B+C and A+C are specified and paired mandatory support to all three 2 UL configurations is FFS.