## Slide 1: WF on CRS-IM demodulation and CSI for non-TM10 TMs
Ericsson, Samsung, NSN, Qualcomm, Huawei, MediaTek
R4-151095
3GPP TSG-RAN WG4 Meeting #74
Athens, Greece, 9th Feb – 13th Feb 2015

## Slide 2: Receiver Structure
Receiver structure defined in Section 4 of TR 36.863 is used as the reference receiver

## Slide 3: Test purposes
To achieve MMSE-IRC+CRS-IC gain with low partial load under homogeneous scenarios.
When the interference condition is not favorable for CRS-IC, there is no performance loss compared with MMSE-IRC when CRS assistance information is provided.

## Slide 4: Test cases
PDSCH demodulation test
  Evaluate tests for following transmission mode
    TM2, TM3, TM4, TM9
  The TMs may be down selected based on test purposes and evaluation results
FFS whether control channel test is needed
    Feasibility of CRS-IM for control channel
    Interested companies may provide some analysis on CRS-IM gain for control channel

## Slide 5: Interference cell modelling
Reusing these FeICIC interference modelling parameters in the CRS-IM tests:
  Number of interference cells
  Time offset and frequency offset
  CRS assistance signaling

## Slide 6: Interference cell modelling (CRS configuration)
Non-colliding CRS shall be included in the tests setup
  the CRS between serving and dominant aggressor/interfering cell as well as CRS between dominant aggressor/interfering cell(s) are assumed to be non-colliding.
Interested companies are encouraged to provide link level analysis for colliding CRS case
  The CRS between the serving and dominant aggressor/interfering cells and/or CRS between dominant aggressor/interfering cell(s) are assumed to be colliding

## Slide 7: Interference cell modelling (Interference level)
The interference level for TM1~TM9 can be selected from 6.3.2 of 36.863 with the following condition:
  Resource utilization
    Option 1: 10%
    Option 2: 20%
    Option 3: 30%
    Option 4: 50%
  The interference set:
    Option 1: the 1st set (corresponding to 5%-tile)
    Option 2: The 10th set (corresponding to 50%-tile)
    Option 3: The 16th set (corresponding to 80%-tile)

## Slide 8: Interference modelling (Partial load modelling)
The partial load can be modelled with the following options:
  Option 1: Random full band (50PRB) on/off model, proportional to the average resource utilization in the interfering cells;
  Option 2: ON/OFF pattern depends on the Possion distribution
The above options are for demodulation. For CSI, the options may be different from demodulation.
Interested companies are encouraged to provide analysis and input for these options.

## Slide 9: Setup for the serving cell
MCS: The following options can be considered:
  Around MCS#5
  Around MCS#14
  Around MCS#20
Interested companies can provide more input on the options in the next meeting

## Slide 10: Interference cell modelling (Antenna configuration)
For antenna configuration, 2x2 shall be included in the test.
  For 4x2 companies can provide analysis in the next meeting

## Slide 11: For CSI
Interested companies are encouraged to provide input on the CSI test regarding at least:
  The feasibility of capturing the CRS-IM gain into CSI derivation
    Clarification on CSI measurement behavior of CRS-IM UE
    Link level simulation results for CSI to justify the feasibility of CSI test.
    How to model partial load in the possible CSI test