## Slide 1: WF on DC SDR test
NTT DOCOMO. INC,…
R4-151115
3GPP TSG-RAN WG4 Meeting #74
Athens, Greece, 9-13 Feb, 2015
Agenda Item: 6.8.1

## Slide 2: Way forward
DC SDR tests
  Specify for both sync DC and sync+async DC UE.
    Apply async DC SDR test when UE supports sync+async DC. If UE supports only sync DC, apply sync DC SDR test.
    Timing offset is 0us for sync DC UE test and 500us for sync+async DC UE test.
  Apply DC SDR test to CA+DC UE on top of CA SDR test.
  Apply DC SDR test to any one of the supported DC configurations covering the largest aggregated bandwidth combination.
  Specifying the DC SDR test for the UE supporting either DC (1A) or DC (3C) or both, and corresponding applicability
    For DC (1A) the TB success rate per CG will be used as text metric

## Slide 3: Annex: DC SDR test cases
DC SDR requirements |  | Configurations
For synchronous capable UE | Supporting DC SCG bearer (1A) | 2UL, 0 time offset
 | Supporting DC Split bearer (3C) | 2UL, 0 time offset
For sync + Async capable UE | Supporting DC SCG bearer (1A) | 2UL, 500 time offset
 | Supporting DC Split bearer (3C) | 2UL, 500 time offset