## Slide 1: WF on DC SDR test
NTT DOCOMO. INC,…
R4-151137
3GPP TSG-RAN WG4 Meeting #74
Athens, Greece, 9-13 Feb, 2015
Agenda Item: 6.8.1

## Slide 2: Way forward
DC SDR tests
  Specify for both sync DC and sync+async DC UE.
    Apply async DC SDR test when UE supports sync+async DC. If UE supports only sync DC, apply sync DC SDR test.
    Timing offset is 0us for sync DC UE test and 500us for sync+async DC UE test.
  Apply DC SDR test to any one of the supported DC configurations covering the largest aggregated bandwidth combination.
  Whether to specify for both DC (1A) supporting UE and DC (3C) supporting UE or not is FFS.

## Slide 3: Annex: DC SDR test cases
DC SDR requirements |  | Configurations
For synchronous capable UE | Supporting DC SCG bearer (1A) or/and Split bearer (3C) are FFS | 2UL, 0 usec offset
 |  | 2UL, 0 usec offset
For sync + Async capable UE | Supporting DC SCG bearer (1A) or/and Split bearer (3C) are FFS | 2UL, 500 usec
 |  | 2UL, 500 usec offset