## Slide 1: Way Forward Proposals for Inter-band CA Consisting of B41
MediaTek Inc., Huawei, ..
3GPP TSG-RAN WG4 Meeting #74
Athens, Greece, February 9th – 13th 2015
R4-151188

## Slide 2: Background
The UE self-desensitization issue for inter-band CA consisting of B41 due to insufficient cross-band isolation was brought up in R4-73AH-0024 [1] and R4-150956 [2]
The existing framework for H/H and L/L CA combinations DTib and DRib relaxations [3] also may not be sufficient to address certain CA combination requirements as brought up in R4-73AH-0100 [4] and R4-73AH-0057 [5], where inter-band CA consisting of B41 can be a good example.

## Slide 3: CA Combinations Consisting of B41
CA Combination | Simultaneous Tx/Rx
CA_39A_41A | No
CA_41A_42A | No
CA_41A_42C | Yes
CA_1A_41C | Yes
CA_26A_41C | Yes
CA_8A_41C | Yes
CA_25A_41C | Yes
CA_3A_41A | Yes

## Slide 4: Observations for CA with B41
#1: For B41 paired with a TDD band, the desensitization would only occur under simultaneous Tx/Rx operation.
#2: For B41 paired with an FDD band, the desensitization may occur when UL is in FDD band, and would only occur under simultaneous Tx/Rx when UL is in B41.
#3: For B41 paired with any low band, no additional relaxation is required except when there is harmonic problem.
#4: Desensitization level can be around 5 dB for B41 and 1.8 dB for its pairing band according to [2].

## Slide 5: Way Forward Proposals
The following WF proposals are intended to address the self-desensitization issue for inter-band CA consisting of B41,
  Proposal 1: RAN4 to study the reference sensitivity degradation for both B41 and its pairing band due to insufficient cross-band isolation based on the available filter (single wideband filter) performance data.
  Proposal 2: For B41 paired with a high-band or 3.5-GHz band with either B41+FDD or B41+TDD supporting simultaneous Tx/Rx, RAN4 to also study additional DTib and DRib required for B41 on top of the existing framework such that no further reference sensitivity relaxation is needed for both B41 and its paring band.
  Proposal 3: Based on the analysis results of Proposal 1 and 2, RAN4 to decide how to define the additional requirements on case-by-case basis.

## Slide 6: References
[1] R4-73AH-0024, “On cross-band isolation of B41+B42+B42 CA UE”, SoftBank Mobile, TSG-RAN WG4 #73AH UE RF Ad Hoc Meeting, Oulu, Finland, January 13th – 16th, 2015
[2] R4-150956, “Way forward proposal for inter-band CA consisting of B41”, MediaTek Inc., TSG-RAN WG4 #74, Athens, Greece, February 9th – 13th, 2015
[3] R4-146833, “Additional framework for Interband CA relaxations”, Nokia Corporation, Telecom Italia, Sprint, Ericsson, TeliaSonera, Orange, Vodafone, TSG-RAN WG4 Meeting #72bis, Singapore, Oct. 6th – Oct. 10th, 2014
[4] R4-73AH-0100, “A closer look at the framework for quadplexed combinations”, Qualcomm Incorporated, TSG-RAN WG4 #73AH UE RF Ad Hoc Meeting, Oulu, Finland, January 13th – 16th, 2015
[5] R4-73AH-0057, “Relaxations of FDD-TDD CA supporting simultaneous Tx/Rx”, MediaTek Inc., TSG-RAN WG4 #73AH UE RF Ad Hoc Meeting, Oulu, Finland, January 13th – 16th, 2015