## Slide 1: Way forward on MMSE-IRC for LTE BS
ZTE, China Telecom, Huawei, Samsung …
R4-151091
TSG RAN WG4 meeting #74
Athens, Greece, 9 – 13 Feb, 2015

## Slide 2: Way forward on scope
On performance requirements of MMSE-IRC receiver for PUSCH:
Prioritize synchronous network, asynchronous network is not precluded.
Prioritize PUSCH to PUSCH collision scenario
Prioritize 1Tx UE scenario over 2Tx UE for both target PUSCH and interference PUSCH.
Only inter-cell interference suppression is considered, i.e. intra-cell inter-user interference resulted from UL MU-MIMO is excluded.
In summary, the first priority for this WI is SIMO PUSCH to SIMO PUSCH collision under synchronous network.

## Slide 3: Way forward on scenarios (1)
Both homogeneous network and heterogeneous network should be considered
  First conduct the homogeneous network evaluation and then conduct the heterogeneous network system level evaluation.
Homogeneous network
  The simulation assumptions should be based on CoMP Scenario 1 in TR36.819
    ISD of the Macro cell is 500m
    Traffic model: full buffer transmission in uplink
ISD for evaluation: 500m
Traffic model: full buffer transmission in uplink

## Slide 4: Way forward on scenarios (2)
Uplink scheduler
  Option 1: The same frequency domain multiplexing method in TR36.814 can be used in the system level simulation for the BS LMMSE-IRC receiver evaluation
  Option 2: PF scheduling and provide the N interferences DIPs per PRB
  Option 3: TDM scheduling (schedule one user per TTI) and provide the N interferences DIPs per PRB
UE dropping
  For homogeneous network simulation: UE dropping 100% outdoor
  For heterogeneous network simulation: UE dropping:20% outdoor and 80% indoor
Cell selection criteria
  RSRP based (no CRE), with 3 dB handover margin
Focus on 1Tx UE case

## Slide 5: Way forward on system-level simulation
The following outputs from the system simulation evaluations should be considered for deciding interference modelling
  Interference power level;
  Number of explicitly modelled interference
Methodologies and statistical measurements
  Use DIP value for evaluation of interference profile.
  Provide the distribution of DIPs considering the following ways:
    Baseline: Unconditional DIP values
    Optional: conditional DIP values
  FFS how to determine DIP values for link level evaluation

## Slide 6: Way forward on reference receiver
  IRC receiver with DMRS based covariance matrix estimation
  Interference covariance matrix estimation should be conducted per PRB and per TTI