## Slide 1: Way forward for UL 64QAM
Huawei, Hisilicon, Nokia Corporation, CMCC
TSG-RAN Working Group 4 (Radio) meeting #74 R4-151243
Athens, Greece February 9th – 13th, 2015 Agenda 7.4

## Slide 2: UE Tx EVM
It is proposed to use [8%] EVM for UL 64QAM as basis to evaluate MPR/A-MPR requirements
Companies can provide system simulation results to verify the system gain for the proposed EVM value in RAN4#74bis meeting

## Slide 3: MPR/A-MPR
Single carrier/inter-band CA
  MPR values for UL 64QAM for contiguous and non-contiguous resource allocation are defined
  Need for dedicated A-MPR for UL 64QAM should be studied
Intra-band CA
  Example CA combination(S) is chosen
  Both MPR and A-MPR need to be defined for UL 64QAM for contiguous and non-contiguous resource allocation

## Slide 4: Annex: simulation assumptions for evaluation of MPR/A-MPR
PA operating point: UTRAACLR1 = 33 dBc @ Pout = 22 dBm for 100RB QPSK signal
Modulator IQ imbalance = 25 dBc
Modulator carrier leakage = 25 dBc
Modulator C_IM3 = 60 dBc
Phase noise=[33] dBc
Transceiver noise= [-29.5] dBc