## Slide 1
3GPP TSG-RAN WG4 #74
Athens, Greece, 9 – 13 Feb, 2015
Agenda item: 9.4.3
Ericsson, Huawei, Nokia Corporation, InterDigital, Verizon, Qualcomm, China Telecom, Alcatel-Lucent, ZTE
Way forward on Adjacent channel coexistence evaluation parameters and methodology for LAA
R4-151270

## Slide 2: Objective
Define adjacent channel coexistence evaluations assumptions and methodology for 5GHz LAA systems
Consider following interference scenarios
  LAA-to-Wifi
  Wifi-to-LAA
  LAA-to-LAA
Reference is Wifi-wifi case
Consider both APs and UEs as transmitters and receivers
Note: this document includes some additional parameters for the adjacent channel coexistence simulations in addition to simulation assumptions in 36.889

## Slide 3: Channel arrangements
Agreement:
Only consider adjacent 20MHz channels for the current evaluations

## Slide 4: Case-1: Wifi-to-LAA
Case-1:
LAA
Wifi
f

## Slide 5: Case-2: LAA-to-Wifi
Case-2:
Wifi
LAA
f
Note:
Condider legacy ACLR for LAA BS, then extend to a range
[30,..., 45]dB

## Slide 6: Case-3: LAA-to-LAA
Case-3:
LAA1
LAA2
f
Note:
Condidering legacy ACLR for LAA, there will not be any need for this evaluation.
However, for BS ACLR ranges [30,..., 45]dB, we need to evaluate this scenario.

## Slide 7: Deployment
Follow 36.889
  Indoor deployment
    In-building, 4 APs per operator, max 2 operators per building
    Operators could be LAA or wifi operators
  Outdoor deployment
    Hotspot kind of deployment
    Each operator has 4 APs inside the hotspot
Channel models
  Follow the models described in 36.889

## Slide 8: Simulation parameters
Deployment
  Same parameters as 36.889, v0.1.1
  Listed in attached doc
Band specific requirements
  Model the transmission power requirements as
    Max TxP
    Example could be 5.150-5.250 GHz band
Wifi ACLR and ACS values
  Companies need to provide and agree on those values offline.

## Slide 9: Evaluation methodology
Static simulations (primarily)
  For closure of SI, RAN4 uses static simulations.
  Focus for Rio meeting is static simulations.
Dynamic simulations
  Assumptions for dynamic simulations will follow the RAN1 assumptions plus adjacent channel RF aspects only if issues are found in static simulation
Evaluation metric, e.g.
  Step-1:Transmission opportunity for LAA at adjacent channel due to wifi interferer
    i.e. To plot the cdf of the total adjacent channel interference (ACI) seen at adajcent channel when an interferer is transmitting on a neighboring carrier
  Step-2: Throughput degradation for victim system due to adjacent channel interferer(s)

## Slide 10: Methodology for static simulations
Deploy the network (Evaluate LAA DL only)
  For LAA to WiFi, we will evaluate LAA DL interferes WiFi DL, and evaluate LAA DL interferes WiFi UL.
  For WiFi to LAA, we will evaluate WiFi DL interferes LAA DL, and evaluate WiFi UL interferes LAA DL.
Assign the carriers to APs
  Assume 2 adjacent carriers
  LAA and Wifi will share the channel fairly
  Wifi UL/DL probability is 50%/50%
Assign users to APs
Evaluate adjacent channel interference seen from neighboring carrier and calculate SINR

## Slide 11: Channel selection procedure
Channel selcetion can be done randomly based on channel sensing
  More details are FFS