## Slide 1: Draft WF for D2D performance requirements
Qualcomm, Huawei, Intel
3GPP TSG-RAN WG4 Meeting #74bis R4-152397
Rio de Janeiro, Brazil, 20th – 24th April 2015

## Slide 2: D2D link performance test
Test purpose
  Verify BLER-SNR performance in fading channel for following D2D physical channels
    PSDCH, PSBCH, PSCCH and PSSCH
  Verify timing and frequency offset handling D2D receiver in following D2D operation scenario
    Intra-cell D2D discovery
    Synchronous inter-cell D2D discovery
    Asynchronous inter-cell D2D discovery
    Intra-cell D2D communication with TA>0 and TA = 0
    Synchronous inter-cell D2D communication with TA>0 and TA = 0
    OOC D2D communication (TA=0)
    Study on other D2D operations scenarios are not precluded
    Separate test case for each operating scenario is not implied
Test set up options
  Consider following options
    Option 1: single side link
    Option 2: multiple side link in different subframes
    Option 3: multiple side link in same subframes
  Multiple options can be chosen

## Slide 3: D2D link performance test
UE RRC state
  Test is defined for UE in idle state or Connected DRX state
Number of cells to be modeled in the test
  Option 1: 1 cell
  Option 2: 2 cells
Channel bandwidth is FFS
Soft buffer combining
  Discovery
    Option 1: define test with 0 HARQ retransmission
    Option 2: define test with 3 HARQ retransmission and soft buffer combining
  Communication
    Define test with soft combining for 3 HARQ retransmissions
CP length
  Normal CP

## Slide 4: D2D link performance test
Tx EVM
  10% Tx EVM is assumed for side link physical signals/channels
AGC operation
  Per-TTI AGC
  AGC settling time
    One symbol for QPSK
    FFS symbols for 16QAM
Channel estimation
  Per-TTI channel estimation
Antenna configuration
  1x2 low correlation
Propagation channel and Doppler fading models are FFS

## Slide 5: D2D link performance test
FRC for PSDCH, PSCCH and PSBCH
  FRC defined in the specification is used
FRC for PSSCH
  option 1: full PRB (25 for 5MHz, 50 for 10MHz) allocation with 16QAM ½
  Option 2: half PRB (12for 5MHz, 25 for 10MHz) allocation for one D2D link, and others for another D2D link
  Other options not precluded
Timing and frequency offset
  Timing and frequency offset is configured based on D2D operation scenario
  In the following slides the models for the selected scenarios are provided
  Companies are encouraged to bring more inputs on the remaining scenarios in the next meeting (timing offset, frequency offset, assumptions on UE synchronization behaviour)

## Slide 6: D2D RX UE Timing Synchronization Behavior: D2D Discovery
Note 1: The timing offset assumption below is to set the FFT window correctly
Note 2: Exact operating scenario may know be known at Rx UE (e.g., intra-cell vs. inter-cell synchronous with common pool)
Operating scenario | Rx reference timing | Timing offset assumption
Intra-cell only | Option 1: Serving cell | *Option 1: [-CP/2 CP/2] *Option 2: [0 CP] *Option 3: [0 2us]
Inter-cell synchronous with common pool | Option 1: Serving cell | *Option 1: [-CP/2 CP/2]
Inter-cell synchronous with non-overlapping Rx pools | Option 1: Serving cell | *Option 1: [-CP/2 CP/2]
 | Option 2: Neighbor cell | *Option 1: [-CP/2 CP/2] *Option 2: [0 CP]
Inter-cell asynchronous | Option 1: SLSS on associated synchronization resource | **Option 1:[-w1 w1] ***Option 1: [-CP/2 CP/2] ***Option 2: [-12Ts 12Ts]
Other options are not precluded
(*) b/w serving cell DL and D2D TX signal at the D2D RX UE
(**) b/w serving cell DL and SLSS signal at the D2D Rx UE
(***) b/w SLSS signal and D2D discovery signal at the D2D Rx UE

## Slide 7: D2D RX UE Timing Synchronization Behavior: D2D Communication
Note 1: The timing offset assumption below is to set the FFT window correctly
Note 2: Exact operating scenario may know be known at Rx UE
Operating scenario | Rx reference timing (for PSCCH) + | Timing offset assumption
Intra-cell only | Option 1: Serving cell | *Option 1: [-CP/2 CP/2] *Option 2: [0 CP] *Option 3: [0 2us]
Inter-cell synchronous with common pool | Option 1: Serving cell | *Option 1: [-CP/2 CP/2]
Inter-cell synchronous with non-overlapping Rx pools | Option 1: Serving cell | *Option 1: [-CP/2 CP/2]
 | Option 2: Neighbor cell | *Option 1: [-CP/2 CP/2] *Option 2: [0 CP]
 | Option 3: SLSS | *Option 1: [-CP/2 CP/2]
OOC | Option 3: SLSS | *Option 1: [-CP/2 CP/2] *Option 2: [-12Ts 12Ts]
Other options are not precluded
(+) PSSCH Rx reference timing is PSCCH timing – TA received in PSCCH
(*) b/w serving cell DL and D2D TX signal at the D2D RX UE
(**) b/w serving cell DL and SLSS signal at the D2D Rx UE
(***) b/w SLSS signal and D2D discovery signal at the D2D Rx UE

## Slide 8: Intra-cell D2D Discovery
Timing offset between Serving cell DL timing and D2D signal arrival timing at the D2D RX UE
  Option 1: [0 2] us
  Option 2: [0 CP] us
  Option 3: +/-1us
  Other options are not precluded
Frequency offset between Serving cell UL and D2D TX UE
  Option 1: +/- 200Hz
  Option 2: +/- 10Hz
  Option 3: +/- 0.1 ppm
  Other options are not precluded
D2D RX UE synchronization behavior
  Serving cell DL timing used as D2D Rx reference timing
  Serving cell frequency used as D2D Rx reference frequency
  UE should perform post-FFT timing and frequency offset compensation

## Slide 9: Inter-cell asynchronous D2D Discovery
Applicability
  UE supporting discovery and SLSS Tx/Rx
Timing offsets between D2D TX, D2D RX and two cellular links are FFS
  Option 1: +/- 3.5 ms between Serving cell DL timing and D2D signal arrival timing at the D2D RX UE
  Other options are not precluded
Frequency offset
  Option 1: +/- 400Hz
  Other options are not precluded
D2D TX UE transmits SLSS
D2D RX UE synchronization behavior
  SLSS timing used as D2D Rx reference timing
  Serving cell frequency used as D2D Rx reference frequency
  UE need to perform post-FFT timing and frequency offset compensation

## Slide 10: Intra-cell D2D communication (TA = 0 and TA > 0)
Timing offset between Serving cell DL timing and D2D signal arrival timing at the D2D RX UE
  Option 1: [0 2] us
  Option 2: [0 CP]us
  Option 3: +/- 1us
  Other options are not precluded
Timing advance between PSCCH and PSSCH for TA > 0
  Option 1: 5us
  Other options are not precluded
Frequency offset between Serving cell UL and D2D TX UE
  Option 1: +/- 200Hz
  Option 2: +/- 10Hz
  Option 3: +/- 0.1 ppm
  Other options are not precluded
D2D Tx UE does not transmit SLSS/PSBCH
D2D RX UE synchronization behavior
  PSCCH and PSSCH with TA = 0: Serving cell DL timing used as D2D Rx reference timing
  PSSCH with TA > 0: Serving cell DL timing - TA received in PSCCH is used as D2D Rx reference timing
  Serving cell frequency used as D2D Rx reference frequency
  UE need to perform post-FFT timing and frequency offset compensation

## Slide 11: OOC communication (TA = 0)
D2D TX UE transmits SLSS/PSBCH
D2D RX UE synchronization behavior
  UE acquires timing and frequency from SLSS/PSBCH from D2D TX UE
    Note 1: SLSS timing measurement accuracy does not exceed ±12 Ts
    Note 2: SLSS frequency measurement accuracy does not exceed ±0.1 ppm
  UE need to perform post-FFT timing and frequency offset compensation

## Slide 12: Power imbalance test
Test purpose
  Verify in-channel selectivity and receiver dynamic range of D2D Rx UE
Test parameters are FFS
  Physical channel
    e.g PSSCH with 2 PRB allocation and QPSK 2/3
  Number of side links transmitted in the same subframe
    e.g. 2 links
  Propagation channel
    e.g. static channel without external noise
  Timing and frequency offset
    e.g. No timing and frequency offset, timing and frequency offset of intra-cell / inter-cell synchronous discovery is applied for each link
  Power imbalance level between side links
    Companies to provide analyses /proposals for power imbalance level to be configured in the test by next meeting

## Slide 13: Maximum side link processes test
Test purpose
  verify maximum side link processes, and maximum data rate (if possible)
Test cases
  D2D Discovery
    Option 1: with 50 sidelink processes
    Option 2: with 50 and 400 sidelink processes
  D2D communication with 16 side link processes
Propagation channel
  static channel without external noise
FRC set up
  Option 1: FRC set configuration in R4-151871
  Companies can bring in other proposals in next meeting
Timing frequency offset
  Option 1: Time/freq offset of 0 w.r.t. serving cell timing/frequency at Rx UE
  Other options not precluded