## Slide 1: WF on EIRP accuracy requirement
NTT DOCOMO,INC., Telecom Italia, Alcatel Lucent, Ericsson, Huawei
3GPP TSG-RAN WG4 Meeting #74-bis R4-152456
Rio de Janeiro, Brazil, 20th – 24th April, 2015 Agenda 7.2.1

## Slide 2: Background
Consideration of EIRP accuracy requirement was provided in WF[1] at RAN4#73.
  There were three open issues as below
  The number of beam pointing directions needed to define the steering range
  How to define the range where the EIRP accuracy requirement is met
  Whether the range in (2.) shall be declared, or interpolation between the maximum steering points, or part of product description (not subject to specification by 3GPP)
According to above and on-line/off-line discussion in RAN4#74bis, WF is proposed in following slides.

## Slide 3: WF(1/2)
  Vendor shall declare
    area or points where EIRP accuracy requirement is met. This area or these number of points are not specified.
    and EIRP values for five points: the zero-steering point and maximum steering points in both directions for θ(0~π) and φ(-π/2~π/2) axis in relation to the coordinate system of AAS BS, where the EIRP accuracy is met.
      There might be overlapped points.
These three points might overlap.
These five points might overlap.
(Max to right)
(Max to up)
(Max to down)
(Max to left)
Zero-steering
φ
θ
φ
θ
φ
θ

## Slide 4: WF(2/2)
  As the core requirement,
    the AAS BS shall achieve an EIRP within +/-XdB of an EIRP value if claimed at any specific point within the declared area or points
      No need to declare EIRP values at all of area or points
  As the conformance requirement,
    measured EIRP should be within +/-(X+TT)dB of the declared EIRP value(s) at five points : the zero-steering point and maximum steering points in both directions for θ(0~π) and φ(-π/2~π/2) axis in relation to the coordinate system of AAS BS. TT (Test Tolerance) is FFS.
      Need to declare EIRP values at five points
      There might be overlapped points.

## Slide 5: Examples (2D steering case)
: declared area
: zero-steering point or one of the maximum steering points
: declared points
and so on..
φ
θ

## Slide 6: Reference
[1] R4-148114, “WF on range of declaration of EIRP”, Huawei, Ericsson, SEI, NEC