## Slide 1: WF on interference modeling for BS MMSE-IRC receiver
China Telecom, Huawei, Nokia Networks, ZTE, Samsung, Alcatel-Lucent
3GPP TSG-RAN WG4 Meeting #74bis R4-152525
Rio de Janeiro, Brazil, 20 - 24 Apr, 2015
Agenda Item: 7.6

## Slide 2: Background
In RAN4 #74 meeting, the following agreements were reached for BS MMSE-IRC receiver:
On inter-cell interference modeling
  The following outputs from the system simulation evaluations should be considered for deciding interference modelling
    Interference power level;
    Number of explicitly modelled interference
  Methodologies and statistical measurements
    Use DIP value for evaluation of interference profile.
    Provide the distribution of DIPs considering the following ways:
    Baseline: Unconditional DIP values
    Optional: conditional DIP values
    FFS how to determine DIP values for link level evaluation
  On reference receiver
  IRC receiver with DMRS based covariance matrix estimation
    Interference covariance matrix estimation should be conducted per PRB and per TTI

## Slide 3: WF (1)
Number of interferers to be explicitly modelled
  In phase-I link-level evaluation, assume two explicitly modelled interferers.
Methodologies to determine DIPs for performance gain tests
  Methodology 1
    Step 1: Decide DIP1. First obtain the distribution of unconditional DIP1 values from all the simulated samples. The DIP1 value at 85%-tile of the DIP1 distribution is taken.
    Step 2: Decide DIP2. For the DIP1 value at 85%-tile, the median of the conditioned DIP2 are obtained, where the median DIP2 is obtained from all DIP2 whose corresponding DIP1 fall within ±5%-tile of 85-tile (i.e., 80~90%).
  Methodology 2
    Step 1: Identify the SINR value at 5%-tile of UL wideband SINR distribution as the SINR of interest.
    Step 2: For each simulated sample, if the UL wideband SINR fall within +/- 0.2 dB of 5%-tile UL wideband SINR, the DIP1/2 values are saved for this sample.
    Step 3: After saving all the conditional DIP1/2 values, the median values of DIP1/DIP2 distribution are taken.
  Note: DIP1 the strongest interferer, DIP2 the second strongest

## Slide 4: WF (2)
Interested companies are encouraged to provide the following results for both homogeneous and heterogeneous scenarios:
  (a) Raw data on UL wideband SINR distribution, unconditional DIP1/2 distributions, for calibration purpose.
  (b) The DIP1/2 values using the methodologies shown in page 3, which will be taken into account for deriving the final DIP values for link evaluation.
  Note 1: Template for collecting the simulation results is provided in R4-152526.
  Note 2: Company results will be collected by email till 9th May.
Interested companies are encouraged to bring proposals on how to check the interference covariance matrix estimation is conducted per TTI per RB.