## Slide 1: WF on CRS-IM PDSCH demodulation non-TM10
Ericsson, […]
R4-152399
3GPP TSG-RAN WG4 Meeting #74bis
Rio de Janeiro, Brazil, April 20th – 24th, 2015

## Slide 2: General setup for CRS-IM
For partial loading modeling, employ per-SF random on/off model in fixed MCS performance test
  Interferers are randomly turned ON independently at each subframe.
  The probability of one interferer is ON at one subframe is equal to the RU
Time delay wrt. Serving cell is [3 us, -1 us] for the 1st and second interference cell.
Frequency shift wrt. serving cell is [300Hz, -100Hz] for the 1st and second interference cell.

## Slide 3: Key parameters for side condition
Resource utilization on the aggressor cells for gain test
  RU=20%
Resource utilization on the aggressor cells for robustness test
  RU = 50%

## Slide 4: Interference profile
Interference profile for gain test
  The 10th set
    [INR1,INR2] = [10.45, 4.6]
Interference profile for the robustness test
  The 1st set
    [INR1,INR2] = [0.19, -1.62]

## Slide 5: Serving cell MCS
Serving cell MCS decision for the gain test need consider the following aspects:
  There should be sufficient CRS-IM gain.
  Test point should be close to serving cell SNR identified in system level study
  There should be no control channel performance bottleneck.
The following options could be considered for the gain/robustness test:
  MCS = 9 or 14 or 18
  Other MCS are not precluded

## Slide 6: Modelling on interference cells
Companies are encouraged to provide input on:
  The transmission mode for the aggressor cells
  The channel model for the aggressor cells

## Slide 7: Test cases
Test cases for the non-TM10 gain test
  TM9
  At least one CRS-based transmission mode among the following TMs:
    TM2
    TM3
    TM4
Test cases for the robustness test
  TM3

## Slide 8: CRS configuration
Non-colliding CRS is configured for the interference cells

## Slide 9: For robustness test
Interested companies are encouraged to provide input on how to perform robustness test
Interested companies can check whether the FeICIC robustness test can serve the purpose

## Slide 10: For antenna configuration
Antenna configuration 2x2 is as baseline.
4x2 is under consideration for further study