## Slide 1: WF on UE synchronization behavior and time-offset modeling
Huawei, Hisilicon, Qualcomm, LGE, Intel
R4-153662
TSG RAN WG4 meeting #75
Fukuoka, Japan, 25 – 29 May, 2015
Agenda Item: 6.5.2

## Slide 2: Way forward
This WF summarizes the common understanding in RAN4 on the UE behavior on reference RX timing and assumptions of timing offset for discovery and communication with different high-layer signaling
Other UE implementation is not precluded

## Slide 3: Discovery
If the “SL-syncConfigIndex-r12” is not configured, or the “SL-syncConfigIndex-r12” and “W2” are configured
  The reference D2D RX timing is serving cell DL timing
  UE would assume timing-offset** between reference D2D RX timing and PSDCH in theory as [-CP/2 CP/2]
If the “SL-syncConfigIndex-r12” and “W1” are configured
  The reference D2D RX timing is SLSS
  UE would assume timing-offset between reference D2D RX timing and PSDCH in theory as [-CP/2 CP/2]
  Neighbour cell DL timing is not precluded to be used as reference D2D RX timing but not assumed to define minimum performance requirements
**: For demodulation requirements, the timing-offset values should take some extra margin into consideration, such as timing error and multiple path delay

## Slide 4: Communication
If the “SL-syncConfigIndex-r12” is not configured
  Serving cell DL timing used as reference D2D RX timing for PSCCH.
    Reference D2D RX timing for PSCCH – D2D TA command received in PSCCH is used as reference D2D RX timing for PSSCH.
  UE would assume timing offset between PSCCH and reference D2D RX timing for PSCCH in theory as [-CP/2 CP/2]
  If the “SL-syncConfigIndex-r12” is configured
  UE assumes the timing offset between PSCCH/PSSCH and reference D2D RX timing as [-CP/2 CP/2] in theory
  Neighbour cell DL timing is not precluded to be used as reference D2D RX timing but not assumed to define minimum performance requirements