## Slide 1: WF on CA_3A-40A/CA_3A-40C
Huawei, Hisilicon, Samsung, Qualcomm, MediaTek, Nokia Networks, LGE, Intel …
R4-153800

## Slide 2: Background (1/3)
Tib/Rib of CA_3A-40A was approved in RAN4#73 using the L-L/H-H framework without any analysis. (R4-146990)
Huawei provided an analysis in RAN4#74 indicating there’s MSD problem for CA_3A-40A. (R4-152254)
MediaTeK provided an analysis in RAN4#75 with similar MSD view. (R4-153063)
TeliaSonera provided an analysis in Thur. evening when RAN4#75 is ongoing. (R4-153875)

## Slide 3: Background (2/3)
MSD proposed by companies
CBW (MHz) | 5 | 10 | 15 | 20
R4-152254 (Huawei) | 3.9 | 3.3 | 2.9 | 2.7
R4-153063 (MediaTek) | 2.8 | 2.8 | 2.7 | 2.7
R4-153875 (TeliaSonera) | 1.3 | 1.2 | 1.2 | 1.2
CBW (MHz) | 5 | 10 | 15 | 20
R4-152254(Huawei) | 4.9 | 4.5 | 4.3 | 4.2
R4-153063 (MediaTek) | 4.6 | 4.1 | 3.9 | 3.8
R4-153875 (TeliaSonera) | 3.0 | 2.8 | 2.7 | 2.6
B3 MSD when B40 Tx transmits signal
B40 MSD when B3 Tx transmits signal

## Slide 4: Background (3/3)
Open issues
  MSD value
  The approach to introduce the new case requirements to the specification
    The whole band will be impacted by the other band regardless the UL location.
    It’s not REFSENS exceptions but REFSENS requirements.

## Slide 5: Way forward (1/3)
Using the following approach to introduce the requirements to the specification

## Slide 6: Way forward (2/3)
MSD value will be put to brackets in one RAN plenary meeting cycle to let other companies further check.
Two options for the MSD value to be put to brackets
  Option1: Average of the 2 inputs before the Tdoc submission deadline of RAN4#75
  Option2: Average of the 3 inputs including the contribution submitted in the Thur. evening in RAN4#75 meeting.
Which option will be used is according to the online discussion.

## Slide 7: Way forward (3/3)
The results of the two options
CBW (MHz) |  | 5 | 10 | 15 | 20
B3 MSD (dB) | Option 1 | 3.4 | 3.1 | 2.8 | 2.7
 | Option 2 | 2.7 | 2.4 | 2.3 | 2.2
B40 MSD (dB) | Option 1 | 4.8 | 4.3 | 4.1 | 4.0
 | Option 2 | 4.2 | 3.8 | 3.6 | 3.5