## Slide 1: WF on D2D Demodulation Performance Test
LG Electronics
3GPP TSG-RAN WG4 Meeting #75
Fukuoka, Japan, 25 – 29 May, 2015
Agenda Item: 6.5.2
R4-153146

## Slide 2: D2D sidelink channel performance test
D2D Discovery
  Verify PSDCH demodulation performance
 | TC1 | TC2
Operating scenario | Intra-cell/Sync inter-cell discovery | Async inter-cell discovery
test purpose / metric | Verify PSDCH / Tput for PSDCH | 
RRC state | Idle | 
# of sidelink | 1 | 
Retransmission | 0 HARQ | 
propagation channel/Doppler | EPA5 / EVA70 | 
FRC / PRB | QPSK / 2PRBs | 
timing offset | [0 CP] | [-w1 w1]
frequency offset | +/- 200Hz | +/- 400Hz
Sync Ref. | serving cell | SLSS

## Slide 3: D2D sidelink channel performance test
D2D Communication
  Verify PSBCH, PSCCH, PSSCH demodulation performance
 | TC3 | TC4 | TC5
Operating scenario | Intra-cell/Sync inter-cell | Intra-cell and async inter-cell | OOC
test purpose | Verify PSCCH and PSSCH | Verify PSCCH, PSBCH, PSSCH | Verify PSSCH
Metric | Tput for PSSCH / BLER for PSCCH | Tput for PSSCH / BLER for PSBCH,PSCCH | Tput for PSSCH
RRC state | C-DRX | C-DRX | Idle
# of sidelink | 1 | 2 | 1
Retransmission | 3 HARQ |  | 
Soft buffer combining | Soft buffer combining |  | 
channel BW | 5/10MHz |  | 
propagation channel and Doppler | EPA5 / EVA70 |  | 
FRC / PRB | QPSK for PSCCH / 1 PRB, QPSK for PSBCH / 6PRBs, 16QAM for PSSCH / full PRBs |  | 
allocation in subframe |  | different subframe | 
timing offset | [0 CP] | [-20 20]msec for inter-cell [0 CP] for intra-cell | [-20 20]msec
frequency offset | +/- 200Hz | +/- 400Hz for inter-cell +/- 200Hz for intra-cell | +/- 400Hz
Sync Ref. | serving cell (No transmit SLSS/PSBCH) | SLSS for inter-cell and serving cell for intra-cell | SLSS
Communication mode | Mode1 (TA > 0) |  | Mode 2 (TA=0)

## Slide 4: D2D sidelink channel performance test
Power imbalance test
  Verify in-channel selectivity and dynamic rage of D2D Rx UE
 | TC6
Operating scenario | Intra-cell discovery
RRC state | Idle
# of sidelink | 2
Retransmission | 0 HARQ
channel BW | 5MHz
propagation channel/Doppler | Static channel
FRC / PRB | 16QAM for PSSCH / 2 PRBs (MCS14 or 20)
allocation in subframe | same
resource pool | common pool
timing offset | 0
frequency offset | 0
Sync Ref. | Serving cell
Power imbalance level | [19] dB

## Slide 5: D2D sidelink channel performance test
Maximum sidelink process
  Verify maximum sidelink process and maximum data rate
 | TC7 | TC8
Operating scenario | Intra-cell Discovery | Intra-cell communication
test purpose | Verify maximum sidelink process and maximum data rate | 
RRC state | Idle | Idle
# of sidelink | 50/400 | 16
Retransmission | 1 HARQ | 3 HARQ
Soft buffer combining | No soft buffer combining | 
channel BW | 5 MHz | 
propagation channel/ Doppler | Static channel | 
FRC / PRB | QPSK | 16QAM for PSSCH