## Slide 1: WF on D2D Demodulation with Multiple sidelinks
LG Electronics, Huawei, HiSilicon, Qualcomm, Intel, Samsung
3GPP TSG-RAN WG4 Meeting #75
Fukuoka, Japan, 25 – 29 May, 2015
Agenda Item: 6.5.2
R4-153676

## Slide 2: Background
Following test cases were agreed in Ad-hoc meeting for multiple sidelinks
  Power imbalance test
  Maximum sidelink processes
FFS for multiple links with different subframe

## Slide 3: WF on Power Imbalance test
Verify in-channel selectivity and dynamic range of D2D Rx UE
Test / Simulation Parameters |  | Test 1 (Discovery) | Test 2 (Communication)
# E-UTRA cells |  | 1 (serving cell) | 
# D2D UEs |  | 2 | 2
D2D UE 1 | Transmission | PSDCH (0 HARQ) | PSCCH/PSSCH
 | PSSCH RMC | N/A | QPSK, TCR 2/3
 | Timing offset w.r.t. serving cell | 0 us | 0 us
 | Freq offset w.r.t. serving cell | 0 Hz | 0 Hz
 | Rx power level | D2D UE2 + [19dB] | D2D UE2 + [19dB]
 | RB allocation (PSDCH/PSSCH) | 2RB[4,5] | 2RB[4,5]
D2D UE 2 | Transmission | PSDCH (0 HARQ) | PSCCH/PSSCH
 | PSSCH RMC | N/A | QPSK, TCR 2/3, 2RBs
 | Timing offset w.r.t. serving cell | 0 us | 0 us
 | Freq offset w.r.t. serving cell | 0 Hz | 0 Hz
 | Rx power level | - | -
 | RB allocation (PSDCH/PSSCH) | adjacent 2 RB of UE1[6,7] | adjacent 2 RB of UE1[6,7]
Leakage model from UE1 Link to UE 2 Link at Rx UE due to ICS for simulations only |  | Option 1 : -19dBc leakage into adjacent 2 RBs, operating SIR is 0dB for UE2 Option 2 : -22dBc leakage into adjacent 2 RBs, operating SIR is 3dB for UE2 Other options are not precluded (Leakage model over entire BW is not needed. This is for simulation purpose to derive the Link 2 operating SIR) | 
Propagation Channel | Serving cell | AWGN | 
 | D2D UE 1 |  | 
 | D2D UE 2 |  | 
Noc |  | -98dBm/15kHz | 
Channel BWs |  | 5MHz | 
Simulation results needed |  | PSDCH BLER for UE 2 link | PSSCH BLER for UE 2 link

## Slide 4: WF on Maximum sidelink process
Verify maximum sidelink process and maximum data rate
Test / Simulation Parameters |  | Test 1 (Discovery; 50 Sidelink Processes) | Test 2 (Discovery; 400 Sidelink Processes) | Test 3 (Communication)
# E-UTRA cells |  | 1 (serving cell) |  | 
# D2D UEs |  | 50 | 400 | 16
D2D UE | Transmission | Option 1: PSDCH (3 ReTx) | Option 1: PSDCH (3 ReTx) | PSCCH/PSSCH
 | PSSCH RMC | N/A | N/A | 5 MHz: 25 PRBs and 18336 TBS 10 MHz: 50 PRBs and 25456 TBS
 | Timing offset w.r.t. serving cell | 0 us | 0 us | 0 us
 | Freq offset w.r.t. serving cell | 0 Hz | 0 Hz | 0 Hz
Propagation Channel | Serving cell | Clean channel |  | 
 | D2D UE |  |  | 
Channel BWs * |  | 5/10/15/20 MHz | 10/15/20 MHz | 5 MHz and 10MHz
Rx UE assumptions (for simulation) | Timing reference | Serving cell |  | 
 | Frequency reference |  |  | 
Resource pool allocation |  | R4-153081(5.1.1., 5.1.2.) |  | R4-152781(2.4)
Simulation results needed |  | PSDCH BLER |  | PSSCH BLER
* UE can only pass maximum channel bandwidth for this test

## Slide 5: WF on Multiple links with different subframe
Test purpose
  To verify the PSDCH or PSCCH/PSSCH performance under different sync reference for multiple links with non-overlapping resource pools
Test configuration
  Two D2D Tx UEs are configured
    One D2D Tx UE is for serving cell, and other D2D Tx UE is for neighbor cell (async inter-cell)
    Rx D2D UE sync reference
      For intra-cell : serving cell
      For inter-cell : SLSS
  Two non-overlapping resource pools (time domain) are configured.
    One is serving cell and other is neighbor cell (async inter-cell)
  Test to allow for lead time for UE to allow for SLSS detection for asynch inter-cell resource pool during which the UE may skip intra-cell D2D.

## Slide 6: WF on Multiple links with different subframe
This table is just information for test configuration.
  Companies are encouraged to provide detail test configuration for next meeting.
Test / Simulation Parameters |  | Test 1 (discovery) | Test 2 (communication)
Applicable operating scenario |  | Intra-cell and Inter-cell asynchronous | 
# E-UTRA cells |  | 2 | 
# D2D UEs |  | 2 | 2
D2D UE 1(inter-cell async) | Transmission | SLSS+PSDCH(0HARQ) | SLSS+PSBCH+PSCCH+PSSCH(3HARQ)
 | PSSCH RMC | N/A | 16QAM, TCR 1/2, fully allocated
 | Timing offset | 1usec+0.5msec (w.r.t. serving cell) | 1usec+10.5msec (w.r.t serving cell)
 | Freq offset | +200Hz (w.r.t. serving cell) | +200 Hz (w.r.t. serving cell)
 | Resource pool | >5msec offset from UE 2 resource pool | >5msec offset from UE 2 resource pool
D2D UE 2 (intra-cell) | Transmission | PSDCH(0HARQ) | PSCCH+PSSCH(3HARQ)
 | PSSCH RMC | N/A | 16QAM, TCR 1/2, fully allocated
 | Timing offset | 1usec (w.r.t. serving cell) | 1usec (w.r.t. serving cell)
 | Freq offset | +200Hz (w.r.t. serving cell) | +200 Hz (w.r.t. serving cell)
Propagation Channel | Serving cell | AWGN | AWGN
 | D2D UE 1 | EPA5 | EVA70
 | D2D UE 2 | EPA5 | EVA70
Channel BWs |  | 10MHz | 
Rx UE assumptions (for simulation) | Timing reference | SLSS for UE1 and serving cell for UE2 | 
 | Timing offset range b/w PSDCH and timing reference | [-CP/2 CP/2] | [-CP/2 CP/2]
 | Frequency reference | Serving cell | 
Simulation results needed |  | PSDCH BLER | PSSCH BLER