## Slide 1: WF on modeling additional UEs in D2D RRM tests
Qualcomm Incorporated, Ericsson
R4-153685
3GPP TSG-RAN WG4 Meeting #75
Fukuoka, Japan, 25-29 May, 2015
Agenda Item: 6.5.1

## Slide 2: Background
Agreed D2D RRM test case list in R4-152315
It was left FFS in R4-152315 if we need to model additional UEs in the RRM tests
  Additional UEs refer to UEs transmitting D2D signals beyond those needed for test purpose
D2D Discovery | 
Test Case | Test purpose
D.1 | Initiation/Cease of SLSS (FDD bands)
D.2 | Initiation/Cease of SLSS (TDD bands)
D.3 | Transmit timing requirement for D2D discovery (FDD bands)
D.4 | Transmit timing requirement for D2D discovery (TDD bands)
D.5 | Interruptions due to D2D discovery (FDD bands only)
D2D Communication | 
Test Case | Test purpose
C.1 | Initiation/Cease of SLSS (In-coverage)
C.2 | Transmit timing requirement for D2D communication with NTA_SL = 0 (In-coverage)
C.3 | Interruption due to RRC reconfiguration for D2D communication (In-coverage)
C.4 | Initiation/Cease of SLSS (Out-of-coverage)
C.5 | Transmit timing requirement for D2D communication (Out-of-coverage)
C.6 | SyncRef UE selection / reselection (Out-of-coverage)
C.7 | Cell identification delay on the DL frequency (Out-of-coverage)

## Slide 3: Way Forward
Add additional UEs to RRM tests which require the UE under test (DUT) to only do D2D reception.
Additional UEs should not be added in tests which require the DUT to do D2D transmission.
Additional UEs shall be modeled using actual D2D transmissions
    PDSCH scheduling pattern to ensure that UE UL transmissions (e.g., ACK/NACK) are not expected on a subframe on which additional UE are transmitting.
D2D Discovery |  |  | 
Test Case | Test purpose | UE under test required to Tx or Rx for D2D | 
 |  | Transmit | Receive
D.1 | Initiation/Cease of SLSS (FDD bands) | x | 
D.2 | Initiation/Cease of SLSS (TDD bands) | x | 
D.3 | Transmit timing requirement for D2D discovery (FDD bands) | x | 
D.4 | Transmit timing requirement for D2D discovery (TDD bands) | x | 
D.5 | Interruptions due to D2D discovery (FDD bands only) |  | x
D2D Communication |  |  | 
Test Case | Test purpose |  | 
C.1 | Initiation/Cease of SLSS (In-coverage) | x | 
C.2 | Transmit timing requirement for D2D communication with NTA_SL = 0 (In-coverage) | x | 
C.3 | Interruption due to RRC reconfiguration for D2D communication (In-coverage) |  | x
C.4 | Initiation/Cease of SLSS (Out-of-coverage) | x | 
C.5 | Transmit timing requirement for D2D communication (Out-of-coverage) | x | 
C.6 | SyncRef UE selection / reselection (Out-of-coverage) | x | 
C.7 | Cell identification delay on the DL frequency (Out-of-coverage) (Test 1) when UE is transmitting for ProSe | x | 
 | Cell identification delay on the DL frequency (Out-of-coverage) (Test 2) when UE is receiving for ProSe |  | x

## Slide 4: Way Forward
D2D Discovery tests with additional UE
  Tests: D.5
  Example # of additional UEs: 12 UEs per subframe (5MHz) on a discovery subframe
    2 RBs per UE
    Same power level in all resource elements
  Example Resource allocation of additional UEs: non-overlapping RBs in a subframe
    NOTE: as depicted on the right
D2D Communication test with additional UEs
  Test: C.3, C.7 (Test 2)
  Example # additional UEs: 12 UEs in a SF (5MHz)
    2 RBs per UE
    Same power level in all resource elements
  Example Resource allocation of additional UEs: non-overlapping RBs in a subframe
    Note: as depicted on the right
  Example PSSCH RMC (5MHz): 2 RBs, QPSK, TCR 1/3