## Slide 1: WF on D2D-WAN concurrency requirements
Ericsson
R4-153851
TSG RAN WG4 meeting #75
Fukuoka, Japan, 25-29 May, 2015
Agenda Item: 6.5.2

## Slide 2: Background
In RAN4#74bis, the group agreed to have test case(s) to verify the WAN performance with D2D/WAN concurrency in R4-152378. According to the agreement, The following test purposes shall be covered in the D2D/WAN concurrency tests.
  Verify no impacts on the downlink demodulation performance.
    In case of concurrent reception of WAN and D2D communication
    (FFS) In case of concurrent reception of WAN and D2D discovery
  Verify uplink transmission prioritization over D2D transmission and reception.
  Verify the downlink reception prioritization over D2D reception
but how to test is open.

## Slide 3: WF on D2D-WAN concurrency requirements
Demodulation test case(s) shall be defined for D2D Communications for D2D-WAN concurrency.
In demodulation test for D2D-WAN concurrency, requirements on WAN reception are defined with the following purpose(s):
    Verify no impacts on the downlink demodulation performance.
    FFS：Verify uplink transmission prioritization over D2D transmission and reception.
    FFS: Verify the downlink reception prioritization over D2D reception

## Slide 4: D2D-WAN Concurrency Test Setup
Test / Simulation Parameters |  | Test 1
Example applicable D2D operating scenario |  | Intra-cell
# E-UTRA cells |  | 1 (serving cell)
RRC state |  | RRC_CONNECTED (non-DRX)
WAN parameters | PDSCH scheduling | FFS (concurrent with PSSCH)
 | PDSCH RMC | FFS (e.g. reuse SDR test parameters)
D2D parameters | # D2D TX UEs | FFS
 | SL-syncConfig configured | Sync config not present
 | Transmission | PSCCH+PSSCH
 | PSSCH RMC | FFS
 | PSSCH scheduling | FFS (concurrent with PDSCH)
 | D2D TX Timing offset | 0us (w.r.t. serving cell)
 | D2D TX Freq offset | +0Hz (w.r.t. serving cell)
 | TA in PSCCH | TA = 0
Propagation Channel | Serving cell | [AWGN / Noise free]
 | D2D TX UE(s) | [AWGN / Noise free]
Channel BWs |  | [5 MHz and 10MHz]
Performance metrics |  | PDSCH Throughput FFS whether PSSCH performance is checked Note: The interruption issue is subjected to RRM decision.

## Slide 5: WF on D2D-WAN concurrency requirements
No Demodulation test cases for D2D discovery to verify D2D-WAN concurrency.